## Slide 1: Planning for Public Transportation and Land-Use
Module 3, Lesson 5

## Slide 2: Learning Objectives
Explain the Transportation and Land-Use Connection
Describe the history of Transportation and Urban Development
Examine the costs of Sprawl
Discuss pedestrian-friendly design and Transit Oriented Development

## Slide 3: Overall Context
Places a focus on the interdependence between the transportation and land-use systems through a discussion of the history of urban transport and urban development, and the costs of sprawl.
Transit Oriented Development is examined as a solution to combat urban sprawl and promote walking, cycling , and public transportation.

## Slide 4: The Transportation and Land Use Connection
Source: adapted from Giuliano (2005)
Transportation
Accessibility
Land Use
Activity Pattern
Notes: Transportation system, travel behavior, and spatial development patterns are interdependent. Transportation infrastructure, programs, and policies influence spatial development patterns. At the same time spatial development patterns shape travel behavior.
For example, construction of a new freeway provides better (faster and easier) accesses to a new part of a metropolitan area. Businesses and households can now locate alongside this new freeway. Low-density development around the new freeway and poor accessibility without a car contribute to car dependence in these new outlying areas.
Similarly, a new light rail corridor may improve accessibility by public transportation. Households and businesses may locate next to one of the light rail stops. Mixed-use and dense development will allow individuals to ride transit or walk and cycle more easily for certain trips.
Even though the transportation and land-use connection seems to be obvious, empirical studies have proven to be difficult and the precise relationship remains still uncertain.
Source: Handy (2005)

## Slide 5: Potential Land Use Responses to Transit Investments
Notes: Transportation investments can influence land use in several ways:
(1) Through improved accessibility, as discussed in slide 4. Accessibility is the focus of most transportation studies. Changes in accessibility influence travel demand and development of new areas.
(2) Complementary policies. New transport infrastructure can ‘spur’ complementary policies and programs that focus on changing land-use patterns. Transport investments provide the impetus for stakeholder involvement, planning, and potentially a new community vision on land use.
(3) The momentum gained through the new investment may attract other investors or community support for land-use changes.
Source: Polzin, 1999.

## Slide 6: Spatial Evolution of U.S. Metropolitan Areas: One Hour Commuting Distance and Different Transportation Modes
(1) Walking-horsecar era (1800-1890)
  Pedestrian walking speed is about at 5 km/h. A circle of about 10 km around the city center could be reached within this time.
(2) Streetcar era (1890-1920)
  Travel speed is around 15 km per hour along fixed lines.
(3) Automobile era (1920-1945)
  Driving (without freeways) at about 30 km/h.
(4) The highway era (1945-now).
  Driving (with freeways). Along freeways 60 km/h are possible
Source: Adapted from Rodriguez 2005, Mueller, 2005
1
2
3
4
Transit line
Urban highway
Notes: The spatial development patterns of American cities co-evolved alongside changes in transportation technology. New transportation modes allowed for new types of developments.
In the 19th century, spatial expansion of the city was limited by distances accessible on foot or by horsecar (for wealthier individuals). Steam railroads also allowed traveling longer distance, but fares were expensive and only affordable for the very wealthy.
(2) Because of comparatively low fares streetcars allowed a larger share of the population to move farther away from the city center following streetcar corridors. Often transit agencies developed land around new transit stations and along new transit corridors.
(3) The advent of the automobile allowed households and businesses to locate away from transit corridors and open new areas between corridors for development.
(4) Today urban freeways allow faster travel and easier access to certain areas of the metropolitan area.
Over the last 60 years American metropolitan areas have been spreading out with declining population densities and large separated single-use residential, commercial and residential areas. The majority of trips in these areas are made by automobile.

## Slide 7: Potential Costs of Sprawl
More Vehicle Miles Traveled
Higher Infrastructure Costs
Adverse Fiscal Impacts
Less Cost-Effective Transit
Loss of Agriculture Lands
Loss of Environmental Lands
Greater Stress
Higher Energy Consumption
Greater City Fiscal Distress
Greater Inner City Deterioration
Source: Burchell et al. 2002
Notes: Commonly cited characteristics of sprawled development are: Poor accessibility (residential and destination); Scattered or leap-frog development; Lack of functional open space (e.g. parks for recreation); Low dense development; Strip development; Scattered development; Lack of mix of land uses; Poor street connectivity (source: Ewing)
Alleged costs of sprawl include:
- More Vehicle Miles Traveled: greater distances between trip origins and destinations and lack of transportation alternatives to automobile use.
- Higher Infrastructure Costs: this includes costs for roads but also for other municipal services, such as sewage or water. In low density areas there are more miles of roads, sewage or water lines per capita—resulting in higher costs to municipalities.
- Less Cost-Effective Transit: provision of public transport is more difficult in low density areas. Everything else equal, lower vehicle occupancy reduces transit’s cost effectives and productivity.
Loss of Agriculture and Environmental Lands: Low density development consumes more land than dense, mixed-use development, thus reducing available land for agriculture and environment.
Higher Energy Consumption: more trips and longer distances traveled by automobile contributes to more energy consumption. Moreover, residential areas with single detached housing consume more energy per capita for heating and cooling than apartments.
Source: Burchell et al. 2002

## Slide 8: Empirical Evidence: Weighted Average Elasticities of Transit Use with Respect to Built Environment Variables
Source: Ewing and Cervero, 2010
Notes: Ewing and Cervero provide an overview of past studies linking land-use to travel behavior. This slide shows relationships of land use indicators with public transportation use. The authors group land-use and built environments in several categories (density, diversity, design, distance to transit).
Density Indicators:
- Measured per unit of gross or net area;
- Different kinds of density: Population, dwelling units, employment, building floor area, or something else. Population and employment are sometimes summed to compute an overall activity density per areal unit.
Diversity:
- number of different land uses in a given area and the degree to which they are represented in land area, floor area, or employment.
- low values indicate single-use environments and higher values more varied land uses
- Jobs to housing or jobs-to-population ratios are less frequently used.
.

## Slide 9: Transit at Destination and Origin
Source: Cervero/TRB, 2005
Notes: Residing and working near rail is associated with the greatest likelihood to commute by rail—even controlling for car ownership.
Residing away from rail and working away from rail is associated with the least likelihood to commute by rail, even after controlling for car access.

## Slide 10: Pedestrian-Friendly Characteristics
Attention to Detail
Accessibility
Comfort/Safety
Human Scale
Definition/Visual Enclosure
Linkage
Complexity/Intricacy
Coherence/Order
Transparency/Human Presence
Sense of Place/Identity
Source: Ewing 1999
Notes: As seen above distance of land-uses to transit are an important determinant of transit use. Roughly 80% of public transportation trips begin or end with a trip on foot.
Thus, designing places for pedestrians can help increase public transportation use. Planning for pedestrian traffic requires different techniques than planning for automobile traffic. This slide shows a short listing of some of these design elements.
-Walking speed is slower than car travel speed. Thus attention to design details along a pedestrian environment are crucial.
-Continuous sidewalks, crosswalks, lowered curbs, low car traffic volumes and pedestrian traffic lights allow for easy and safe pedestrian access.
- Separation from traffic or low car traffic speeds increase pedestrian safety and comfort.
- A built environment that provides a sense of enclosure in the form of a ratio building height to width of roadway + sidewalk or street enhances human scale and provides visual enclosure.
- Linking public places and walkways with each other—often through mid-block short cuts provides attractive pedestrian access.
- Complex scenes that appeal to all senses (including water fountains or musicians) make a place walkable.
- Transparent street frontage of buildings (e.g. shop or office shop windows) make a place transparent and provide the feeling of human presence.
- Design elements can link the TOD to the history of a place or provide an identity for a place.

## Slide 11: Transit Oriented Development (TOD)
“An environment around a transit stop or station that supports pedestrian and transit use, created by providing a mix of land uses in a safe, clean, vibrant, and active place.” (New Jersey DOT)
“Is a mix of housing, retail and/or commercial development and amenities – typically referred to as mixed-use development – integrated into walkable neighborhoods within a half-mile of quality public transportation.” ( Reconnecting America)
Notes: Transit Oriented Development is one tool to encourage more dense mixed-use development around transit stops.
Even though a new concept, TOD is not a new idea. Transit systems in the late 19th century and early 20th century were often involved in developing land in station areas of new transit corridors.
Today, most TODs in the USA are built around rail (37% regional rail, 31% light rail, 22% commuter rail) (Source: Cervero, Reconnecting America, CTOD). One reason is the perceived of ‘permanence’ of rail tracks compared to bus routes that may be changed more easily. There are international examples of bus rapid transit (BRT) and TOD, such as Curitiba, Brazil and Bogota, Columbia.

## Slide 12: Transit Oriented Development (TOD)
“Moderate- to higher-density development, located within an easy walk of a major transit stop, generally with a mix of residential, employment, and shopping opportunities designed for pedestrians without excluding the automobile. TOD can be new construction or redevelopment of one or more buildings whose design and orientation facilitate transit use. “ (California DOT)
Transit oriented development (TOD) generally refers to higher-density development, with pedestrian priority, located within easy walking distance of a major public transit station or stop(s). (TCRP Report 95)
Notes: Currently, there exists no universally accepted definition for TOD, as can be seen from the definitions above.
Planning for TOD requires coordinating the needs of a node in the transit network and the needs of an attractive place to live and work.
Node—point on the network where riders can access public transport.
Place—attractive, vibrant neighborhood that promotes sustainability, social interaction. 9Source: TCRP Report 102)
Often a 10 minute walking distance (600-800m) around a station is used as boundary for TOD (Renne, 2010). But development next to Transit is not necessarily TOD.
Transit Adjacent Development is near transit (walking distance), but lacks features that promote transit use, other than proximity (e.g. poor ped. environment, single uses)
Transit Oriented Development:
  Walking distance to transit
  Development (re)shaped by transit (e.g. mix of uses, building orientation, parking etc.)
  (Source: Cervero, Reconnecting America, CTOD)

## Slide 13: Potential Benefits of TOD
Reduced household driving and thus lowered regional congestion, air pollution and greenhouse gas emissions
Walkable communities that accommodate more healthy and active lifestyles
Increased transit ridership and fare revenue
Potential for added value created through increased and/or sustained property values where transit investments have occurred
Improved access to jobs and economic opportunity for low-income people and working families
Expanded mobility choices that reduce dependence on the automobile, reduce transportation costs and free up household income for other purposes
Sources: Reconnecting America
Notes: Potential Benefits of TOD include:
“- Increasing the opportunities for residents and workers to meet daily needs by taking transit or walking.
- Attracting new riders to public transit, including so-called “choice” riders—riders who could otherwise choose to drive.
- Shifting the transit station mode of access to be less reliant on park-and-ride and more oriented to walking.
- Reducing the automobile ownership, vehicular traffic, and associated parking requirements that would otherwise be necessary to support a similar level of more traditional development.
- Enhancing the environment, through reduced emissions and energy consumption derived from shifts in commuting, other trip making, and station access to environmentally friendly travel modes.
Non-transportation objectives may include providing desirable and affordable housing choices, enhancing sense of community and quality of life, supporting economic development or revitalization, shifting development from sensitive areas, minimizing infrastructure costs, and reducing sprawl. Financial return is among the motivating factors for at least some of the stakeholders, including, in some cases, the transit agencies involved. Rents, for example, are potentially a significant source of non-farebox revenue accruing from development on system-owned land adjacent to transit stations (Cervero et al., 2004). This chapter is primarily concerned with the travel behavior effects of TOD and thus affords only limited attention to non-transportation objectives.”
Taken from TCRP Report 95.

## Slide 14: A Taxonomy of TODs I
Source: Reconnecting America & CTOD. 2008. Station Area Planning. How To Make Great Transit-Oriented Places. TOD 202.
Notes: Not all TODs are the same. Different characteristics will require different implementation strategies.
“Regional Centers are the regional downtowns, and are characterized by a dense mix of housing and employment types, retail and entertainment that cater to the regional market. They are served by a rich mix of transit modes that support all this activity, including high-capacity regional rail and bus, and local-serving bus. Densities are typically higher within a quarter-mile radius of stations than within the half-mile radius.
Urban centers contain a mix of residential, employment, retail and entertainment uses, usually at slightly lower densities and intensities than in regional centers. Destinations draw residents from surrounding neighborhoods. These centers serve as commuter hubs for the larger region and are served by multiple transit options, often including rail and high-frequency regional bus or bus rapid transit (BRT), as well as local-serving bus. Many urban centers retain their historic character, having preserved both historic buildings and street networks. Densities are typically higher within a quarter-mile radius of stations than the half-mile radius.
Suburban Centers contain a mix of residential, employment, retail and entertainment uses, usually at intensities similar to that found in urban centers but lower than that in regional centers. Suburban centers can serve as both origins and destinations for commuters. They are typically connected to the regional transit network and include a mix of transit types — regional rail and bus, BRT, and local bus — with high-frequency service. Development here may be more recent than that found in urban centers, and there are more single-use employment areas and residential neighborhoods. The intensity of uses is often noticeably greater within a quarter-mile radius of stations than in the half-mile radius.
Transit Town Centers function more as local-serving centers of economic and community activity than either urban or suburban centers, and they attract fewer residents from the rest of the region. A variety of transit modes serve transit town centers, and there is a mix of origin and destination trips – primarily commuter service to jobs in the region. There is less secondary transit service than the previous place types. Secondary transit lines feed primary lines, often at intervals timed to facilitate transfers at the primary transit stations. Residential densities are usually lower than in the previous place types, but there is still a good mix of both multi-family and single-family residential, as well as a mix of retail, smaller-scale employment, and civic uses. Densities are usually noticeably greater within a quarter-mile of transit stations than the half-mile radius. “
Taken from: Reconnecting America & CTOD. 2008. Station Area Planning. “How To Make Great Transit-Oriented Places,” TOD 202

## Slide 15: A Taxonomy of TODs Continued
Source: Reconnecting America & CTOD. 2008. Station Area Planning. How To Make Great Transit-Oriented Places. TOD 202.
Notes: “Urban Neighborhoods are primarily residential areas that are well-connected to regional centers and urban centers. Densities are moderate to high, and housing is usually mixed with local-serving retail. Commercial uses are limited to small businesses or some industry. Development is usually oriented along a well-connected
street grid that is served by a secondary transit network. Transit is often less a focal point for activity than in the “center” place types, and stations may be located at the edge of two distinct neighborhoods. Many urban neighborhoods were developed before World War II as “streetcar suburbs” that grew up transit-oriented. Densities are usually higher immediately adjacent to the primary transit stations but spread more evenly throughout the half-mile radius.
Special use or employment districts are often single-use – either they are low to moderate density employment centers, or are focused around a major institution such as a university, or an entertainment venue such as a stadium. Transit stations are not a focus of economic activity. Secondary transit service is infrequent and
focused on stations; development tends to be more recent, and the street grid may be less connected than in older neighborhoods. There can be significant opportunities for mixed-use development if these stations are well-connected to other parts of the region and there is demand for housing. Densities are usually evenly distributed throughout the half-mile radius around stations.
Mixed use corridors are a focus of economic and community activity but have no distinct center. These corridors are typically characterized by a mix of moderate-density buildings that house services, retail, employment, and civic or cultural uses. Many were developed along streetcar lines or other transit service. Mixed-
use corridors are especially suitable for streetcars, bus rapid transit or other high-quality bus service with closely-spaced stops. Residential development is usually characterized by newer, denser development along the corridor, with older, lower-density homes just off the main strip. Mixed-use corridors are sometimes served by transit stations that create nodes of activity, but these are less distinct than in other types of places, and they are served by networks of secondary transit such as local bus. Mixed-use corridors offer a good opportunity for infill and mixed-use development, and development is usually more intense within a quarter-mile of transit stops.
Transit Neighborhoods are primarily residential areas that are served by rail service or high frequency bus lines that connect at one location. Densities are low to moderate and economic activity is not concentrated around stations, which may be located at the edge of two distinct neighborhoods. Secondary transit service is less frequent and less well-connected. There is often not enough residential density to support much local-serving retail, but there are often retail nodes. Transit
neighborhoods are found within older urbanized areas that were developed as streetcar suburbs and in more recently developed suburban neighborhoods. Transit
neighborhoods can offer significant development opportunities with potential to provide residents with more housing, retail, employment and mobility options, as in urban neighborhoods. Densities are usually evenly distributed in the half-mile radius around stations. “
Taken from: Taken from: Reconnecting America & CTOD. 2008. Station Area Planning. How To Make Great Transit-Oriented Places. TOD 202

## Slide 16: Planning for TOD at 3 Different Scales
Station Area Scale
Corridor Scale
Regional Scale
Source: Reconnecting America 2010. Station Area Planning.
Notes: “Planning for TOD most often takes place at the station area level, and this is where it’s easiest to understand local benefits such as reduced transportation costs for residents, and the creation of a sense of place and community.
A transit corridor is best defined as the walkable areas around all of the stations along a transit line. Any transit technology can define a transit corridor – heavy or light rail, streetcar, trolley or bus. The area of influence along light and heavy rail corridors is typically a half-mile radius around stations. Because streetcars can stop as often as every street corner they tend to have a stronger influence on development all along the line and up to threes blocks on either side
Planning at the regional scale serves to integrate regional goals, such as decreasing traffic congestion and improving public health, with regional contexts, such as a
consideration of population growth and the location of major employment centers.
STATION AREA Planning:
One transit station at a time
Between parcel level planning and regional planning
Steps:
Develop clear land-use alternatives: Developing options for different development scenarios should occur early in the planning process to allow for public discussion and input by community members, property owners and other key stakeholders.
Understand market demand: Plans should understand the market demand for higher-density housing and employment. Where plans include a retail or mixed-use component, including local-serving stores, the feasibility of these uses should be analyzed.
Forecast ridership using TOD modeling tools: TOD modeling tools should be used where feasible to estimate the changes in ridership that will result from the different development alternatives (the provision of parking, levels of development, transit access, etc.).
Minimize land-use conflicts: Potential land use conflicts with adjacent industrial or residential uses should be minimized. The plan should be an opportunity to decide if current industrial uses should be preserved for jobs or goods movement, or if they should be allowed to redevelop as other uses.
Analyze the impact of zoning requirements on potential densities: Zoning provisions such as lot coverage, setbacks and height limits may make it difficult to achieve the densities envisioned in the plan.
Set minimum allowable density standards: While many zoning codes specify a range of densities or a maximum density, setting minimum densities can help define what qualities as TOD and provide flexibility to accommodate market demand.
Locate key services near stations: Key social services like childcare centers, health clinics and other important destinations should be located close to heavily used transit stations and hubs to accommodate the transit-dependent.

## Slide 17: Planning Fundamentals For TOD
1. Maximize ridership through appropriate development.
2. Generate meaningful community involvement.
3. Design streets for all users.
4. Create opportunities for affordable and accessible living.
5. Make great public spaces.
6. Manage parking effectively.
7. Capture the value of transit.
8. Maximize neighborhood and station connectivity.
9. Implement the plan and evaluate its success.
Source: American Planning Association (http://www.planning.org/pas/brochure/pdf/quicknotes.pdf

## Slide 18: Development Guidelines by Type of TOD I
Source: Reconnecting America & CTOD. 2008. Station Area Planning. How To Make Great Transit-Oriented Places. TOD 202.
Notes: Note: this slide and the next slide provide a lot of detail and can be dropped from presentations that focus on an overview.

## Slide 19: Development Guidelines by Type of TOD II
Source: Reconnecting America & CTOD. 2008. Station Area Planning. How To Make Great Transit-Oriented Places. TOD 202.

## Slide 20: A TOD Residential Building Typology
Source: Reconnecting America & CTOD. 2008. Station Area Planning. How To Make Great Transit-Oriented Places. TOD 202.

## Slide 21: A TOD Mixed Use/Employment Building Typology
Source: Reconnecting America & CTOD. 2008. Station Area Planning. How To Make Great Transit-Oriented Places. TOD 202.

## Slide 22: A TOD Open Space Typology
Source: Reconnecting America & CTOD. 2008. Station Area Planning. How To Make Great Transit-Oriented Places. TOD 202.

## Slide 23: Empirical Findings: TOD, Travel Behavior, Land Use, and Transit System
TOD commuters typically use transit two to five times more than other commuters; TOD transit commute share can vary from 5% to near 50%
Transit share of all trips in TOD is two to five times higher than outside TOD, but mode shares only 2% to 20%
Transit system extensiveness and level of service are positively correlated with transit ridership; Transit service headways of 10 minutes seem to support a transit lifestyle,
For commutes, proximity to rail stations is a stronger influence on transit use than land use or quality of walking environment. Location of jobs accessible by transit influences ridership
Factors that most influence transit ridership are station proximity, transit quality, and parking policies.
  Fast, frequent, and comfortable transit service will increase ridership, as will high parking charges and/or constrained parking supply
  The availability of free or low-cost parking is a major deterrent to transit ridership
Source: TCRP Report 128
Notes: Travel impact depends on:
-relative travel times compared to the automobile.
-extensiveness of transit service (more opportunities increase transit use).
-TOD type (e.g., suburban neighborhood versus suburban center) is less important than specific location within the region and the quality of connecting transit service .
-There is no rule of thumb or single mode share number that can be easily applied to a hypothetical new TOD along a new rail or bus system. This is due to widely varying local travel conditions and employment distributions.
-HOWEVER: The transit mode shares are statistically reliable, and for an existing rail system, one could reasonably infer the approximate transit mode share of a hypothetical new TOD by comparing it to similar TODs in the same system.
A primary reason for higher TOD transit use is self-selection. Current transit users and those precluded to use transit seek out TOD. The travel pattern of TOD residents prior to moving to the TOD depended on their previous access to transit. When work location was unchanged, often a significant percent (e.g., 50%) were transit users. Among commuters with no previous transit access, transit use increased (up to 50%).
Source: TCRP 128
Other Empirical findings:
  Portland
  Over 30% of Portland TOD residents commute by transit at least once a week and 23-33% used transit as their primary commute mode. (compared to < 10% in the automobile-oriented suburbs, and 15% overall). (Dill 2006)
  Nearly 16% of Portland TOD commuters switched from non-transit to transit modes. (Dill 2006)
  DC
  Transit mode shares along the Washington Metro system were found to decrease by 7 percentage points for every 1,000 feet of distance from a station in the case of housing and by 12 percentage points in the case of office worker commute trips. (Evans and Pratt 2007)
  Arlington
47% of residents use modes of travel other than the automobile to get to work
73% arrive at rail stations on foot, providing a cost savings because neither the county nor WMATA have to provide long-term commuter parking
About 40,000 riders board daily at the ﬁve urban stations in the Rosslyn-Ballston Corridor
About 29,000 riders board at the four suburban stations farther out along the Orange Line; only 15% of these transit riders arrive at their stations on foot, while 58% arrive by car

## Slide 24: However, it remains difficult to isolate the effect of TOD empirically, because of….
Many confounding factors
Long time horizons
Residential self-selection
Generative or redistributive benefits
Negative impacts on property values (e.g. noise)
Network aspect of location of TOD
Source: TCRP Report 128, Curtis et al. 2010.
Notes: Confounding factors include:
a lot of parking in TOD
A primary reason for higher TOD transit use is self-selection. Current transit users and those precluded to use transit seek out TOD. The travel pattern of TOD residents prior to moving to the TOD depended on their previous access to transit. When work location was unchanged, often a significant percent (e.g., 50%) were transit users already. Among commuters with no previous transit access, transit use increased (up to 50%).
Generative or redistributive benefits:
-Higher retail sales in TOD vs. lower retail sales in auto-oriented mall are redistributive
-Concentrating development around a train station vs. same development along a highway-> are there truly new benefits due to TOD?
-Boarnet (1998) finds that a highway investment shifted economic activity within a region
-Travel time saving due to reduced congestion might be generative benefit
Negative Impact:
  Properties near stations may also experience negative impacts such as noise, congestion, pollution, and accidents, because of a concentration of traffic
  Armstrong (1994) found that Boston homes located in census tracts with rail stations had 6.7 percent higher selling prices while proximity to the line (within 400 feet) coincided with a 20 percent decrease in value (potentially
  related to freight trains).
  Landis, Guhathakurtakurta, and Zhang (1994) find a negative impact of being close to Caltrain line; no problems for light rail
  Lastly, proximity and accessibility to the urban core influence potential development capacity of TOD. Locations close to the urban core or with easy access to the urban core have more development potential than TOD in outlying areas with poor accessibility to the core.
  Source: TCRP Report 128, Curtis et al. 2010.

## Slide 25: Comparison of TOD housing and ITE vehicle trip generation rates (24 hour estimates)
Notes: Note: this is a technical slide and does not have to be included in this lecture.
Two publications of the Institute of Transportation Engineers (ITE) are often used in local transportation planning—particularly by local jurisdictions without their own travel surveys or data collection. The publication “Trip Generation An ITE Informational Report” reports on the number of vehicle (automobile/SUV/light truck) trips generated for different types of land uses. Vehicle trip generation rates are based on empirical counts in mainly suburban locations. Thus, these rates do not account for land uses close to public transportation. The table above compares vehicle trip generation rates from the ITE publication and local counts close to public transport. It shows that land uses in TODs generate fewer vehicle trips than typical land uses in the ITE publication. Similarly, ITE’s publication “Parking Generation: An ITE Informational Report” reports on rates of vehicle parking spaces needed. These rates are mainly based on suburban locations during peak parking times. Land-uses close to transit likely have lower parking requirements.

## Slide 26: Impediments to TOD by Stakeholder Group
TCRP Report 102
Notes: This slide lists potential barriers for the implementation of TOD (Source: TCRP Report 102).
Land Prices --
Location – existing rail lines often follow unattractive routes
Real estate market cycles
Non-supportive government policies (e.g. local zoning)
Institutional barriers (private vs. public; coordination across governments and agencies)
Not In My Back Yard (NIMBY)
Congestion
Parking standards
Congestion:
Development concentrated in one area invariably adds more traffic and lowers levels of service
  But overall regional vehicle miles traveled (VMT) and congestion levels will fall with time
  Distinction “good vs. bad congestion”
  Short term vs. long term
  Parking:
Rigid (high) parking requirements can make TOD financially infeasible
Unbundling parking can promote affordable-housing objectives and create a more walking-friendly environment
Also parking availability at stations (again node vs. place)

## Slide 27: Potential Government Support for TOD
Federal:
  Legislation (e.g. New Starts, Transportation and Community and Systems Preservation Pilot Program);
  Center for Transit-Oriented Development;
  Funding for state and regional planning.
States:
  Promote regional and state-wide coordination;
  Provide financial incentives;
  Remove regulatory and statutory barriers to land use;
  Provide planning, policy research, technical assistance, and information for municipalities;
  Pilot programs.
TCRP Report 102
Notes: Policies at federal, state, and local levels of government can help promote TOD (Source: TCRP Report 102).
FEDERAL
New Starts ratings are based on (among others) Growth management; Transit supportive corridor policies; Supportive zoning regulations near transit stations; and Tools to implement land use policies.
CTOD helps:
  develop standards and definitions for transit-oriented development adjacent to public transportation facilities
  system planning guidance, performance criteria, and modeling techniques for MPO
  and research support and technical assistance to public transportation agencies, metropolitan planning agencies, and other persons regarding transit-oriented development;
  Transportation and Community and Systems Preservation Pilot Program (e.g. NJ, $800,000 for 11 municipalities to study TOD feasibility)
STATE
Forge collaborative working relationships among state entities such as transportation, transit, highways, community development, and housing;
  Implement programs and funding initiatives (often using federal dollars) that achieve these goals;
  TCRP Report 102

## Slide 28: Potential Government Support for TOD
Regional
  Promote regional coordination for transportation and land-use planning;
  Provide financial incentives;
  Setting regional visions and policy goals.
Local:
  Zoning (reduced parking, mixed use, minimum densities, density bonuses, overlay zones);
  Planning;
  Reduced Fees;
  Siting Government Facilities.
TCRP Report 102
Notes: Policies at federal, state, and local levels of government can help promote TOD (Source: TCRP Report 102).
FEDERAL
New Starts ratings are based on (among others) Growth management; Transit supportive corridor policies; Supportive zoning regulations near transit stations; and Tools to implement land use policies.
CTOD helps:
  develop standards and definitions for transit-oriented development adjacent to public transportation facilities
  system planning guidance, performance criteria, and modeling techniques for MPO
  and research support and technical assistance to public transportation agencies, metropolitan planning agencies, and other persons regarding transit-oriented development;
  Transportation and Community and Systems Preservation Pilot Program (e.g. NJ, $800,000 for 11 municipalities to study TOD feasibility)
STATE
Forge collaborative working relationships among state entities such as transportation, transit, highways, community development, and housing;
  Implement programs and funding initiatives (often using federal dollars) that achieve these goals;
  TCRP Report 102

## Slide 29: Possible Roles for the Transit Agency in Support for TOD
Brokers, facilitators, educators
Funders, active development partners
Advocates
Land and land assembly
Infrastructure investment
Shared parking
Direct financial participation
TCRP Report 102
Notes: Transit agencies should provide good transit service. But above and beyond that transit agencies can also:
“Factors that most inﬂuence transit ridership are station proximity, transit quality, and parking policies.
Fast, frequent, and comfortable transit service will increase ridership.
High parking charges and/or constrained parking supply also will increase ridership.
Free or low-cost parking is a major deterrent to transit ridership.
Successful strategies include: TOD transit pass programs, parking reductions, and car-sharing programs
TOD transit programs will be similar to other transit programs. Because by definition TOD residents and households are the nearest to transit, TODs should be among the ﬁrst locations that transit agencies implement specialized programs.
TOD (e.g., mixed uses, high densities, reduced parking) is still illegal around station areas in many cities and transit districts
Steps transit agencies are taking to promote TOD include: reconsidering replacement parking requirements at park and rides, advocating for zoning changes with TOD entitlements, land assembly, joint development, and educational efforts (e.g., producing TOD guidebooks)”
Taken from TCRP Report 102

## Slide 30: Suggested Readings
Arrington, G.B., Cervero, R. 2008. TCRP Report 128: Effects of TOD on Housing Parking and Travel. National Academies, Transportation Research Board, Transit Cooperative Research Program, Washington, D.C. (available online, read summary only, pp. 1-5)
Burchell, R., Lowenstein, G., Dolphin, W.R., Galley, C., 2002. Costs of sprawl 2000, TCRP Report 74. Transportation Research Board. National Academy Press, Washington D.C. (available online, read executive summary only, pp. 1-20)
Ewing, R., Cervero, R., 2010. Travel and the Built Environment: A Meta Analysis. Journal of the American Planning Association 76(3), 265 - 294.
Polzin, S. 1999. Transportation/Land-use Relationship: Public Transit’s Impact on Land Use. ASCE Journal of Urban Planning and Development, December 1999, pp. 135-151.
TRB, 2001. Making transit work: Insight from Western Europe, Canada and the United States. Transportation Research Board, National Research Council, National Academy Press, Washington DC. (available online, read chapter 2 only).

## Slide 31: More Resources
Arrington, G.B., Cervero, R. 2008. TCRP Report 128: Effects of TOD on Housing Parking and Travel. National Academies, Transportation Research Board, Transit Cooperative Research Program, Washington, D.C.
Black, A., 1995. Urban Mass Transportation Planning. McGraw-Hill, New York City.
Burchell, R., Lowenstein, G., Dolphin, W.R., Galley, C., 2002. Costs of sprawl 2000, TCRP Report 74. Transportation Research Board. National Academy Press, Washington D.C.
Curtis, C., Renne J., Bertolini, L., 2009. Transit Oriented Development: Making It Happen. Ashgate Publishing, Burlington.
Cervero, R., Ferrell, C., Murphy, S. 2002. Transit-Oriented Development and Joint Development in the United States: A Literature Review. National Academies, Transportation Research Board, Transit Cooperative Research Program, Washington, D.C.
Cervero et al. 2004. TCRP Report 102: Transit Oriented Development in the United States-Experiences, Challenges, and Prospects. National Academies, Transportation Research Board, Transit Cooperative Research Program, Washington, D.C.
Ewing, R., Cervero, R., 2001. Travel and the built environment. A synthesis. Transportation Research Record 1780.
Ewing, R., Cervero, R., 2010. Travel and the Built Environment: A Meta Analysis. J. Am. Plann. Assoc. 76(3), 265 - 294.
Ewing, R., 1999. Pedestrian- and Transit-Friendly Design: A Primer for Smart Growth. Smart Growth Network, Washington, D.C.

## Slide 32: More Resources
Handy, S. 2005. “Smart growth and the transportation - Land use connection: What does the research tell us?” International Regional Science Review. 28 (2), pp. 146-167.
Hanson, S., Giuliano, G., 2004. The geography of urban transportation, 3rd ed. The Guilford Press, New York.
Moore, T., Thorsnes, P., Appleyard, B., 2007. The Transportation/Land Use Connection. American Planning Association, Chicago.
Muller, P.O., 2004. Transportation and urban form: Stages in the evolution of the American metropolis, In: Hanson, S., Giuliano, G. (Eds.), The geography of urban transportation. Guilford Publications, New York.
Polzin, S. 1999. Transportation/Land-use Relationship: Public Transit’s Impact on Land Use. Journal of Urban Planning and Development, December 1999, pp. 135-151.
Reconnecting America, 2008. TOD 202 Station Area Planning. Reconnecting America/ Center for Transit Oriented Development.
Reconnecting America, 2010. TOD 203 Transit Corridors and TOD. Reconnecting America/ Center for Transit Oriented Development.
Reconnecting America, 2011. TOD 204 Planning for TOD at the Regional Scale. Reconnecting America/ Center for Transit Oriented Development.
TRB, 2001. Making transit work: Insight from Western Europe, Canada and the United States. Transportation Research Board, National Research Council, National Academy Press, Washington DC.
Vuchic, V., 1999. Transportation for livable cities. Center for Urban Policy Research (CUPR), New Brunswick, NJ.

## Slide 33: Walkability Assignment
About 80% of passengers access public transportation on foot. For this assignment you will grade the streets/built environment adjacent to a public transportation station (or hub) according to pedestrian friendly design criteria. You can choose a station/hub close to your campus or you can use online software with street view features (e.g. google maps or bing maps) to access stations elsewhere in the United States. You should employ pedestrian friendly design criteria introduced during today’s lecture and/or some of those listed in the reading by Reid Ewing (see link below).
First, you should develop your own tool to measure walkability/transit accessibility. Criteria can include: human scale (signs, height to width ratio), buffering (trees, parking distance to street), street furniture, space (wide, long views, complex scenes), etc. Once the tool is developed you should score the street(s) close to the transit stop on all of your indicators on a scale from 1 to 5 (5 is best). You can evaluate the street in person or via street view features of google, bing, or others.

## Slide 34: Walkability Assignment
Deliverables:
Measurement instrument for pedestrian friendly design. In a short write-up you should explain how your measurement instrument works; this includes connections between constructs (e.g. buffering from car traffic) and measurements (e.g. spacing of street trees, presence of parked cars).
Overall and criterion score for the street(s) (ideally with pictures or screenshots from the street).
Short text summarizing your justification for the score given to the street(s). This text should explain why you decided to give your score; this should ideally be connected to the readings or class discussion.
Excel table summarizing your individual scores of the streets.
Suggestions for (realistic) improvements for the street for more pedestrian friendliness.
Evaluation of the performance of your tool (1 or 2 paragraphs). What were the problems? How would you improve it?
Note: you can work in groups to develop the tool, analyze the results, and write the text. However, each student has to score the street(s) him or herself. Groups should then present average scores across all group members and indicate potential diverging scores across group members.
Link to the Ewing (1999) text: http://www.epa.gov/smartgrowth/pdf/ptfd_primer.pdf

## Slide 35: Walkability Tool Example

## Slide 36: Links
Rail~Volution: http://www.railvolution.org/
CTOD (Center for Transit Oriented Development): http://www.ctod.org/
Reconnecting America: http://reconnectingamerica.org/

## Slide 37: Sources:
Notes: This slide lists the main sources for this presentation. You can find a detailed list of references on the last slide of this presentation. The detailed text in the lecture notes generally originates from these sources.