## Slide 1: Network Characteristics
Module 3, Lesson 3

## Slide 2: Learning Objectives
Understand how technology traits should match the market characteristics
Be able to describe the different network configurations including overlaying modes, radial/crosstown/timed transfer
Describe the integration of multiple modes including park and ride, bikes on buses and airport/intercity

## Slide 3: Overall Context
Transit systems often include aspects of the radial, grid, and timed transfer concepts in their design characteristics.

## Slide 4: Metropolitan Area Travel
  Diverse origins and destinations
  Auto access available for virtually any O/D pair at any time of day
  Traditional Central Business Districts generally represent less than 10% of the region’s overall travel market
  To attract a large market share, transit must appeal to non-CBD travel
  A challenge for transit to “organize” diverse travel patterns into functional transit lines.
Notes: Use this time to relate back to urban transportation modeling in general. Demand for transit trips is constrained by supply because transit does not go everywhere at every time. Demand for auto trips is generally not constrained by supply – there may be congestion that affects the trip time but you can still get to any place where there is a road.

## Slide 5: Typical Regional Travel Patterns
Notes: From a Portland metropolitan plan from the 1980s and should be updated.

## Slide 6: Transit’s Competitive Situation (Conceptual Mode Choice Curve)
Notes: Vuchic

## Slide 7: “Ubiquitous” (Everywhere to Everywhere) System Probably Not Affordable
Notes: Thompson, G.L. (1977). Planning considerations for alternative transit route structures. Journal of the American Institute of Planners, 43, 158-168.

## Slide 8: Systemwide Network Concepts
Traditional CBD Radial Networks
Grid Networks
Timed Transfer Networks

## Slide 9: Traditional Radial Concept
Notes: Thompson, G.L. (1977). Planning considerations for alternative transit route structures. Journal of the American Institute of Planners, 43, 158-168.

## Slide 10: Radial Network Characteristics
  Historical orientation to traditional city center
  Where the densest concentration of jobs are (were?)
  Higher congestion and parking prices; comparative advantage for transit
  Service for > 90% of region’s trips not oriented to CBD
  Travel through CBD (in and out)
  “Reverse” commute generally not equivalent service (highest frequency is peak time peak direction)
  Circumferential routes (similar to highways)
Notes: Can still make an argument that radial is the “best” approach but clearly limits upside of transit use forever.
FYI. Thompson paper classifies transit systems as radial and non-radial:
Service Orientation, Bus–Rail Service Integration, and Transit Performance
Examination of 45 U.S. Metropolitan Areas
Jeffrey R. Brown and Gregory L. Thompson
Transportation Research Record: Journal of the Transportation Research Board,
No. 2042, Transportation Research Board of the National Academies, Washington,
D.C., 2008, pp. 82–89.

## Slide 11: Grid System
Notes: Thompson, G.L. (1977). Planning considerations for alternative transit route structures. Journal of the American Institute of Planners, 43, 158-168.

## Slide 12: Grid System Characteristics
Provides service for “many-to-many” O-D pairs without connecting every pair directly
  No out of direction travel
  But, a transfer is required for many trips (high ratio of unlinked to linked trips)
Requires high frequency service throughout the grid at all times of day and on weekends
System does not have to be a literal grid (i.e., right angles) to work functionally as a grid

## Slide 13: Grid System
Notes: Paris

## Slide 14: Grid System
Notes: London

## Slide 15: Timed Transfer (Focal Point) System
Notes: Thompson, G.L. (1977). Planning considerations for alternative transit route structures. Journal of the American Institute of Planners, 43, 158-168.

## Slide 16: Timed Transfer Characteristics
Allows for “many-to-many” travel but at lower cost than full grid
  Or could be used to supplement grid during off peak times
May require 2 transfers
  Airline hub analogy (small city to small city)
Multi-centered systems
  Rail stations as hubs for transfers between buses
  Activity centers (malls, colleges, etc.) w/all day use

## Slide 17: Timed Transfer (Focal Point) System
Some Rules:
Most lines on identical Headways (H)
Travel time between TCs should be a multiple of H
Some flexibility, but if H varies, longer/shorter must be an Integer
Requires operational discipline to guarantee connections

## Slide 18: Timed Transfer (Focal Point) System
Notes: Vuchic

## Slide 19: Timed Transfer (Focal Point) System
Notes: Vuchic

## Slide 20: Timed Transfer (Focal Point) System
Notes: Thompson – need to get source

## Slide 21: Grid System Maximum Headway Theorem
15 Minutes is the maximum headway for:
  Random arrival at a stop or station, and therefore
  Transferring on a ubiquitous transfer network (grid)
Notes: Tom Matoff (asserted based on experience)

## Slide 22: Grid System Maximum Headway Corollary
Grid service on a 15-minute maximum headway, or shorter, is the best service.
However………

## Slide 23: Maximum Headway Corollary (cont’d)
If a 15-minute headway cannot be sustained, better service is provided by a timed transfer system based on a maximum system headway of 30 minutes.

## Slide 24: Grid and Timed Transfer Networks
Require attention to Physical Detail
Relationship of Network Concept to Physical/Project Design
Transit or Transfer Centers required (Infrastructure Intensive)

## Slide 25: Grid and Timed Transfer Networks
Notes: Vuchic

## Slide 26: Grid and Timed Transfer Networks
Like the Grid System, the Timed Transfer System has an important network property……….
They concentrate CBD ridership (and some other major market ridership) on a few lines in select corridors

## Slide 27: Concentrating Travel Volumes Can Reduce Operating Cost
Notes: Source?

## Slide 28: Multiple Mode Trips
Circulator shuttle (bus, van, people mover)
  Corporate
  Neighborhood
  Downtown
Low Demand Areas
  Flexible-route minibus or van
  Demand Response vehicle
  Taxi

## Slide 29: Multiple Mode Trips (cont.)
Park and Ride
  Relatively small operating cost for transit system
    Lot security and upkeep <<$ feeder bus service
    Costs borne by auto drivers who park there
  Requires large area for surface lots or high cost structure
    Limits station area development / TOD potential
  Reduced benefits (emissions, cost of auto use, etc.)

## Slide 30: Multiple Mode Trips (continued)
Bicycling
  Lockers, bike racks at stations
  Bike stations (safe storage and repair)
  Bike sharing
  Bike racks on buses
  Storage locations on rail cars
The “last mile” problem
  Often a problem where density not adequate to support attractive level of regular transit service
Notes: More information about bike transit integration:
http://www.nctr.usf.edu/jpt/pdf/JPT12-3Pucher.pdf
http://policy.rutgers.edu/faculty/pucher/TRBJan2010.pdf

## Slide 31: Other Network Considerations
Connections to inter-city hubs
  Airports
  Train Station (High-Speed Rail)
Special events
  Stadiums, arenas, festivals
    Often very occasional use (handful of events each year) but very large volumes
    Can provide wider support for facilities (even if only use the service once a year)

## Slide 32: Network Structure Summary
Transit systems often include aspects of the radial, grid, and timed transfer concepts
Heaviest travel link(s) in network may be considered as corridor(s) for higher volume modes such as rail or BRT