## Slide 1: Module 4, Lesson 4
Developing Service: Measuring Quality of Service
Notes: Unless otherwise indicated, the source for all content in this module is the 2003 NTI course “Transit Capacity and Quality of Service Short Course.”

## Slide 2: Learning Objectives
Differentiate between transit performance viewpoints, including those of the passenger, the community, and the agency
Summarize the various metrics that can be used to evaluate transit quality of service

## Slide 3: Transit Performance Metrics

## Slide 4: Transit Performance Viewpoints
What aspects of transit performance might each of these groups be most interested in?
  Transit passengers
  The transit agency
  Motorists and roadway agency staff/decision-makers
  The community as a whole
Notes: In your work as a service planner you will represent the views of the transit agency – but these other viewpoints are valid and should be considered as well.

## Slide 5: Transit Performance Viewpoints
Quality of service focuses on the passenger point of view
Other points of view are also valid and need to be considered
  May have conflicting objectives (e.g., passenger comfort vs. agency resources)
  Best-quality passenger service may not be feasible or desirable
Notes: The concept of “Quality of Service” means evaluating service from the passenger perspective.
Quality of Service measures can counterbalance an agency’s focus on its internal needs and bring the focus back to the customer.

## Slide 6
Notes: This figure shows examples of the types of measures used in the transit industry, and the points-of-view they relate to. Some measures relate to more than one point-of-view.
“Quality of service” focuses on the passenger point of view.
Click once to bring up a circle highlighting the passenger’s areas of concern: Service Availability and Comfort & Convenience.
Source: Transit Capacity and Quality of Service Manual 4-5

## Slide 7: Transit Agency Performance Measures
Passenger trips (unlinked) per revenue hour
Passenger trips (unlinked) per revenue mile
Operating expense per vehicle revenue hour
Operating expense per vehicle revenue mile
Operating expense per unlinked passenger trip
Operating expense per passenger mile
Farebox recovery ratio – percent of operating expenses covered by fares
Subsidy per passenger trip – dollars of operating expenses NOT covered by fare
Notes: The precise metrics that your agency emphasizes will vary based on agency priorities.
Farebox recovery ratio standards vary significantly by the type of service provided. The goal might be as low as 20% or as high as 40%.
Note that the number of unlinked passenger trips will NOT be the same as the number of individuals using the system. Transit commuters will be using the service at least twice a day – more if you consider transfers.

## Slide 8: Motorist Point of View
Measure vehicle speed, capacity, delay
Well-established methods for calculating these measures (Highway Capacity Manual)
Includes measures of roadway capacity in terms of the number of transit vehicles that can be accommodated
All vehicles are treated equally, regardless of the number of passengers being carried
Notes: These measures look at individual vehicles. For transit riders, they can reflect the passenger’s point-of-view, because passengers are riding in the vehicles, but when used to make decisions, they can work against transit, because there are typically many more passenger vehicles than transit vehicles on the roadway system.

## Slide 9: Community Point of View
Measure impact of transit service on individuals and community as a whole
  Ability to access, hold a job
  Personal, community economic benefits
  Property values
  Development impacts
  Environmental costs/benefits, etc.
Mobility benefits
  Extent of travel choices
Notes: The community point of view measures transit’s role in meeting broad community objectives.

## Slide 10: Passenger Point of View
Assess the availability and convenience of transit service as seen by passengers
Availability measures are typically under an operator’s control, but limited by funding
Comfort and convenience measures
  Influenced by equipment choices
  Influenced by external factors (e.g., traffic congestion)
Notes: Passenger-based measures directly measure the passenger point-of-view and are the focus of transit quality of service.

## Slide 11: Quality of Service
The overall measured or perceived performance of transit service from the passenger’s point-of-view
  Service availability
  Comfort and convenience
Notes: QOS measures focus on measuring service availability and comfort & convenience. The fixed route QOS framework incorporates six measures. An overall multimodal LOS can be calculated which incorporates automobile, pedestrian, bicycle and transit LOS (see Chapter 17: Urban Street Segments of the Highway Capacity Manual 2010). Because the transit LOS component incorporates many of the factors included in the fixed route QOS framework, it is also useful for analyses where a range of transit QOS factors are desired to be evaluated, but only a single transit LOS letter is desired as an output.
Source: Transit Capacity and Quality of Service Manual, 3rd Edition, 4-6

## Slide 12: Quality of Service Framework
Availability
Service Frequency
Hours of Service
Access
Comfort and Convenience
Passenger loads
Reliability
Travel time
Six transit service measures
Notes: The QOS framework provides six service measures, grouped into two areas: availability, and comfort and convenience. These measures apply to fixed route transit, though there is a similar framework for demand responsive transit as well.

## Slide 13: Availability
How often is service provided?
Service Frequency
Access
Hours of Service
Notes: One measure of service availability is frequency.

## Slide 14: Headway
Average Headway (min) | Frequency (bus /h) | Passenger Perspective | Operator Perspective
≤ 5 | ≥ 12 | Schedules not needed | Feasible for high density corridors Exclusive right-of-way highly desirable
5 – 10 | 6 - 12 | Schedules not needed | Feasible for high density corridors Exclusive right-of-way highly desirable
11 - 15 | 4 - 6 | Maximum desirable wait time if service missed | Feasible in higher density corridors, routes with strong anchors on both ends and park-and-ride based peak-period commuter service
16 – 30 | 2 - 4 | Must adapt travel to schedule, resulting in less than optimal arrival or departure times | Feasible in moderate density corridors Typical commuter rail headway; longest commuter bus headway
Notes: Headway is the service measure; frequency given for comparison.
Clock headways preferable to customers for less-frequent service (>10 minutes).

## Slide 15: Headway
Average Headway (min) | Frequency (bus /h) | Passenger Perspective | Operator Perspective
31 - 59 | 1 - 2 | Must adapt travel to schedule, resulting in less than optimal arrival or departure times | Typically 40- or 45-min headways Feasible in low-to-moderate density corridors
60 | 1 | Minimal service to meet basic travel needs | Typical minimum headway for fixed-route service
> 60 | < 1 | Undesirable for urban transit service due to typical long waits for return trips and when a bus is missed | Some form of demand-responsive transit may better meet passengers’ travel needs
Notes: Headway is the service measure; frequency given for comparison.
Clock headways preferable to customers for less-frequent service (>10 minutes).

## Slide 16: Availability
How long is service provided?
Service Frequency
Access
Hours of Service
Notes: Service availability is measured using hours of service.
Travelers will only use a transit route if service is available near the time they need to leave – as well as the time they need to make their return trip.

## Slide 17: Hours of Service
Hours per day | Passenger Perspective | Operator Perspective
> 18 | A full range of trip purposes can be served | May require added driver pay for late-night work May require increased security measures
15 – 18 | Allows a broad range of trip purposes to be served (e.g., night classes, shift work, early morning flight trips) | May require more than two full-time drivers of overtime pay
12 – 14 | Serves work trips based on traditional office hours with some flexibility | Can be covered by two full-time drivers per vehicle

## Slide 18: Hours of Service
Hours per day | Passenger Perspective | Operator Perspective
7 – 11 | Allows trips to be made during the middle of the day At the upper end of the range, still not enough service for someone working traditional office hours who needs flexibility | Provides sufficient work for full-time drivers, or two part-time drivers
4 – 6 | With peak period service allows some choice of a.m. and p.m. departure times | Provides sufficient work for part-time drivers
< 4 | Basic lifeline service that allows a round trip in one day or half a day Passengers’ days must be planned around the transit schedule, with little or no flexibility | Might be provided on rural routes with only a few daily departures Buses and drivers may need to alternate between routes to use resources effectively

## Slide 19: Measuring Hours of Service
Example: Service departs a location every half-hour between 5:30 a.m. and 8:00 p.m.
  15 hours of service (round up)
Example: Peak hour service with trips at 6:30 a.m., 7:30 a.m., 4:30 p.m., and 5:30 p.m.
  4 hours of service
Notes: The basic procedure is to count the number of hours during the day that have service. The method described here formalizes how to do this, when working with a schedule book.

## Slide 20: Availability
Where is service provided?
Service Frequency
Access
Hours of Service
Notes: Service availability over a system is measured using access.

## Slide 21: Access
Service Level | Passenger Perspective | Operator Perspective
> 90% of service area population served | Transit serves nearly all destinations within a community Travel time may be long, as routes wind and loop through neighborhoods | Operator has made a policy decision to emphasize coverage over cost-efficiency Portions of route covering low-density areas likely to be unproductive
> 90% of transit-supportive area served | Transit serves nearly all higher-density areas within the community Destinations located in lower-density areas may not be accessible | May be inefficient to serve some areas
75 – 90% of transit-supportive area served | Most destinations within higher-density areas are served, but not all | Balances coverage and cost-efficiency objectives
Notes: Note:
This is best done with GIS software. It requires transit stop or route locations, as well as population and employment data for relatively small areas. You can obtain from the local planning model and/or Census population data. You may need to subdivide some large zones. The method is described in more detail in the TCQSM.

## Slide 22: Access
Service Level | Passenger Perspective | Operator Perspective
50 – 74% of transit supportive area served | A majority of destinations within higher-density areas are served Walking and bicycling to transit likely to be longer | Potential opportunity to add service
< 50% of transit-supportive area served | Service is typically provided only in the highest-density corridors What service is provided is likely to be relatively direct, resulting in relatively short travel times | Operator prioritized cost-efficiency over coverage
Notes: Note:
This is best done with GIS software. It requires transit stop or route locations, as well as population and employment data for relatively small areas. You can obtain from the local planning model and/or Census population data. You may need to subdivide some large zones. The method is described in more detail in the TCQSM.

## Slide 23: Comfort & Convenience
Will I get a seat when the bus or train arrives?
  Sitting?
  Standing?
Passenger Loads
Travel time
Reliability
Notes: Comfort & convenience is measured using passenger loads.
This reflects passengers’ ability to find a seat and overall crowding levels within a vehicle. More crowding results in longer dwell times, affecting capacity, reliability, and travel time.

## Slide 24: Passenger Loads
Service Level | Passenger Perspective | Operator Perspective
< 50% seated load | No passenger need sit next to another Perceived travel time = actual travel time | Unproductive service if occurs at maximum load point in peak direction
50 – 80% seated load | Passengers have some freedom where can sit Perceived travel time = actual travel time | Marginally productive service if occurs at maximum load point in peak direction
80 – 100% seated load | All passengers can sit Perceived travel time up to 1.1x actual travel time | Productive service Often used as a standard for commuter rail and commuter bus

## Slide 25: Passenger Loads
Service Level | Passenger Perspective | Operator Perspective
Up to 125% seated load | Up to 20% of passengers must stand Perceived Travel time up to 1.25x actual travel time for seated passengers, up to 2.1x for standees | Very productive service Time to serve boarding and alighting passengers goes up when standees are present
Up to 150% seated load | Up to 1/3 of passengers must stand Difficult for boarding and alighting passengers to get on/ off Perceived travel time up to 1.4x actual travel time for seated passengers, up to 2.25x for standees | Very productive service Maximum design load for peak-of-the-peak conditions High potential for boarding and alighting delays
> 150% seated load | Crush loading conditions Passengers may choose to wait for the next vehicle or drivers may choose to pass up stops Perceived travel times continue to go up | Likely to generate complaints about overcrowding and pass-ups Longer dwell times compared to lower loading levels

## Slide 26: Comfort & Convenience
Will I get to my destination on time?
  Measure on-time performance if headway > 10 min
  Measure headway adherence if headway ≤ 10 min
Passenger Loads
Travel time
Reliability
Notes: Comfort & convenience is measured based on service reliability.
On-time performance is used for service operating at greater than 10-minute headways. Headway adherence is used for headways of 10 minutes or less, when regularity of service becomes more important.

## Slide 27: On-Time Performance
On-Time Performance | Passenger Perspective | Operator Perspective
95-100% | One not-on-time vehicle every two weeks* | Achievable by transit services operating below capacity on a grade-separated guideway with few infrastructure or vehicle problems
90-94% | One not-on-time vehicle every week* | Achievable by transit services operating on a grade-separated guideway
80-89% | Up to two not-on-time vehicles every week | Typical range for commuter rail, light rail with some street running and bus services in small to mid-sized cities
* Passenger making one round trip per weekday with no transfers

## Slide 28: On-Time Performance
On-Time Performance | Passenger Perspective | Operator Perspective
70-79% | Up to three not-on-time vehicles every week* | Typical range for light rail with a majority of street running Achievable by bus services in large cities
<70% | Service likely to be perceived as highly unreliable | May be best possible result for mixed traffic operations in congested CBDs
* Passenger making one round trip per weekday with no transfers

## Slide 29: Headway Adherence
Coefficient of Variation | Probability of Being Off-Headway by ½ Headway or More | Passenger and Operator Perspective
0.00 – 0.21 | ≤ 2% | Service provided like clockwork
0.22 – 0.30 | ≤ 10% | Vehicles slightly off headway
0.31 – 0.39 | ≤ 20% | Vehicles often off headway
0.40 – 0.52 | ≤ 33% | Irregular headways, with some bunching
0.53 – 0.74 | ≤ 50% | Frequent bunching
≥ 0.75 | ≥ 50% | Most vehicles bunched
Notes: Applies to average scheduled headways of 10 min or less

## Slide 30: Comfort & Convenience – Travel Time
How much longer will my trip take, compared to driving?
Passenger Loads
Travel time
Reliability
Notes: Comfort & convenience at the system level is measured by comparing transit and auto travel times.

## Slide 31: Travel Time
Based on door-to-door trip times
For transit, need to account for:
  Travel time to and from transit stops
  Waiting time for transit
  Transfer time (if any)
For autos, need to account for:
  Walking time to/from location where car is parked
Notes: Typical values: 2-3 min walk time to/from transit, ½ headway wait time for frequent service (<=10 min), or square root of headway for longer service
Image:
http://www.flickr.com/photos/herrvebah/5190587344/

## Slide 32: Travel Time
Transit-Auto Travel Time Ratio | Passenger Perspective | Operator Perspective
≤ 1 | Faster by transit than auto | Feasible when transit operates in separate right-of-way and the roadway network is congested
> 1 – 1.25 | Comparable in-vehicle travel times For a 40-min commute transit takes up to 10 min longer | Feasible with express service Feasible with limited stop service in an exclusive lane or right-of-way
> 1.25 – 1.5 | Tolerable for choice riders For a 40-min commute transit takes up to 20 min longer | 
Notes: As of 2009, the US average auto trip took 26 minutes, while the average transit trip took 59 minutes (Transit-Auto Travel Time Ratio of 2.3)

## Slide 33: Travel Time
Transit-Auto Travel Time Ratio | Passenger Perspective | Operator Perspective
> 1.5 – 1.75 | Round trip up to 1 hour longer by transit for a 40-min one-way trip | 
> 1.75 – 2 | A trip takes up to twice as long by transit than by auto | May be best possible result for mixed traffic operations in congested downtown areas
> 2 | Tedious for all riders | May be best possible result for small city service that emphasizes coverage over direct connections

## Slide 34: Other Performance Measures
Travel speed
Service regularity
Service directness
  Ratio of transit route distance to shortest roadway distance
  Ratio of transit travel time to automobile travel time
  Percent of travel time spent deviating from direct route
Notes: Service regularity is the % of intervals between transit vehicles that exceed the scheduled headway.

## Slide 35: Other Performance Measures
Amenities provided
  Implement through agency policy/design standards
Comfort
  Satisfaction, environment surveys
Security
Notes: The reliability measures are used as service measures for route segments, and will be discussed in the next set of slides.