## Slide 1: Module 4, Lesson 5
Developing Service: Calculating Capacity
Notes: Unless otherwise indicated, the source for all content in this module is the 2003 NTI course “Transit Capacity and Quality of Service Short Course.”

## Slide 2: Learning Objectives
Describe how to calculate transit vehicle and passenger capacity at four levels:
  Loading area
  Bus stop
  Bus facility
  Person capacity

## Slide 3: Vehicle Capacity

## Slide 4: Why Study Transit Capacity?
Planning (long-range, special event, etc.)
Forecasting the effects of changes in fare policies, or changing vehicle types
The same factors that influence capacity also influence speed and reliability
Analyzing the operation of major transit facilities in large cities
Notes: Capacity issues affect all sizes of systems—whether just on one particular route, or for service to the county fair

## Slide 5: Vehicle Capacity – Bus
The number of buses that can be served by a loading area (bus berth), bus stop, bus lane, or bus route during a specified period of time.
Notes: Definition of vehicle capacity from the TCQSM

## Slide 6: Bus Capacity Relationships
Bus Stop Capacity
Bus Facility Capacity
Loading Area Capacity
Notes: The bus capacity calculation process has three main steps. The capacity of individual loading areas at a bus stop influences the overall bus stop capacity. The critical bus stop capacity influences the bus facility capacity.
(A “loading area” is a position at a curb where a bus can load and unload passengers. A bus stop will consist of one or more loading areas.)
Note that if you desire person capacity rather than vehicle capacity, this adds one more step.

## Slide 7: Loading Area Capacity Factors
Dwell time
Variability of dwell times among buses
Time needed to re-enter street
Capacity/reliability trade-offs
Traffic signal timing
Bus Stop Capacity
Bus Facility Capacity
Loading Area Capacity
Notes: These are the key factors that will affect the capacity of a loading area.

## Slide 8: Bus Stop Capacity Factors
Loading area capacity
Number of loading areas provided per stop
Bus Stop Capacity
Bus Facility Capacity
Loading Area Capacity
Notes: To move from loading area capacity to bus stop capacity, you must take into consideration the number of loading areas provided.

## Slide 9: Bus Facility Factors
“Critical” bus stop capacity
Amount of traffic, bus congestion
Operating practices
Bus Stop Capacity
Bus Facility Capacity
Loading Area Capacity
Notes: To move from bus stop capacity to bus facility capacity, you must identify the critical bus stop and consider delaying factors such as traffic congestion.

## Slide 10: Two Methodologies
Planning methodology
  Use for long-range planning, when exact values for capacity factors aren’t known
  Use for “back-of-envelope” calculations, when a quick, reasonable answer is wanted
Operations methodology
  Mathematical method
  Use for short-term planning and operations applications
  Use when accurate values for capacity factors are known
Notes: There are two options for determining the capacity of a loading area. The simplest one is the planning method – it just involves looking up an approximate capacity on a graph.
The more rigorous option is the operations method – this uses a mathematical equation to calculate a more precise value of the capacity.

## Slide 11: Loading Area Capacity Planning Methodology
Notes: The planning methodology is the simplest option.

## Slide 12: Bus Lane Service Volumes
Notes: Source: TCQSM 6-21

## Slide 13: Passenger Volume
Assumes peak hour factor of 1.00 – appropriate values should be used to reduce these values to reflect passenger flow variations
Notes: Source: TCQSM 6-21

## Slide 14: Loading Area Capacity Operations Methodology
Notes: The operations methodology is equation-based and produces more accurate results.

## Slide 15: Capacity Calculation Process
Step 1: Define the Facility
Step 3: Set a Design Bus Stop Failure Rate
Step 2: Gather Input Data
Step 4: Determine Dwell Time
Step 5: Determine Loading Area Capacity
Step 6: Determine Bus Stop Capacity
Step 7: Determine Facility Bus Capacity
Step 8: Determine Facility Person Capacity
Final bus stop on facility?
No
Yes
Notes: The bus capacity calculation process has eight main steps. The capacity of individual loading areas at a bus stop influences the overall bus stop capacity. The critical bus stop capacity influences the bus facility capacity.
(A “loading area” is a position at a curb where a bus can load and unload passengers. A bus stop will consist of one or more loading areas.)

## Slide 16: Step 1 – Define the Facility
L
L
S
F
L = loading area, S = bus stop, F = bus facility
Bus
Bus
L
L
S
Step 1: Define the Facility
Step 3: Set a Design Bus Stop Failure Rate
Step 2: Gather Input Data
Step 4: Determine Dwell Time
Step 5: Determine Loading Area Capacity
Step 6: Determine Bus Stop Capacity
Step 7: Determine Facility Bus Capacity
Step 8: Determine Facility Person Capacity
Final bus stop on facility?
No
Yes
Notes: As introduced earlier, bus capacity is calculated for three key locations:
Bus loading areas
Bus stops
Bus facilities
For a capacity analysis, a facility can be defined as a discrete piece of infrastructure (e.g. a median busway), a defined section of roadway (e.g. the portion of a downtown street between two defined cross-streets) or the streets followed by a particular route (e.g. a BRT route). Hence a facility can include a mix of operating environments and be used by multiple bus routes with different stopping patterns. All bus stops along the defined length of the facility need to be included in the analysis.
Importantly, all bus stops located along the defined length of the facility need to be included in the analysis, as individual bus stop characteristics are inputs to the bus speed methodology. In addition, bus operations issues can occur at any stop, not just the busiest stop, so it is necessary to evaluate each stop along the facility for potential problems.

## Slide 17: Step 2 – Gather Input Data
Bus Stop Demand Data
Bus Stop Location Data
Skip-Stop Data (if applicable)
Step 1: Define the Facility
Step 3: Set a Design Bus Stop Failure Rate
Step 2: Gather Input Data
Step 4: Determine Dwell Time
Step 5: Determine Loading Area Capacity
Step 6: Determine Bus Stop Capacity
Step 7: Determine Facility Bus Capacity
Step 8: Determine Facility Person Capacity
Final bus stop on facility?
No
Yes
Notes: Bus stop demand data
  Average (mean) dwell time
  Dwell time variability
  Failure rate
  Passenger demand peak hour factor
Bus stop location data
  Position relative to the roadway
  Position relative to an intersection
  Bus stop design type
  Number of loading areas
  Bus facility type
  Traffic signal timing
  Curb lane traffic volume
  Right-turning traffic volume and capacity
  Parallel pedestrian crossing volume
  Skip-stop data
  Number of stops in the stopping pattern
  Bus arrival pattern
  Traffic volume and capacity of the adjacent lane

## Slide 18: Step 3 – Set Design Stop Failure Rate
Sets how often a bus should arrive at a stop only to find all loading areas occupied
  Downtown – rate of 7.5% to 15% recommended
  Outside downtown – rate of 2.5% recommended
Step 1: Define the Facility
Step 3: Set a Design Bus Stop Failure Rate
Step 2: Gather Input Data
Step 4: Determine Dwell Time
Step 5: Determine Loading Area Capacity
Step 6: Determine Bus Stop Capacity
Step 7: Determine Facility Bus Capacity
Step 8: Determine Facility Person Capacity
Final bus stop on facility?
No
Yes
Notes: Bus loading area capacity is maximized when a bus is available to move into a loading area as soon as the previous bus vacates it. However, this condition is undesirable for several reasons: (a) bus travel speeds are reduced, due to the time spent waiting for a loading area to become available; (b) bus schedule reliability suffers because of the additional delays; and (c) buses block traffic in the street while waiting to enter the bus stop. The more often that bus stop failure occurs, the higher the bus throughput over the course of the hour, but the more severe the operational problems.
Consequently, bus capacity analysis incorporates the concept of a failure rate that sets how often a bus should arrive at a stop only to find all loading areas occupied. The selection of a design failure rate sets the bus stop's design capacity-the number of buses that can be served in an hour at a desired level of operational reliability. The design failure rate should balance capacity and operational needs. Suggested values are as follows:
In downtown areas, design failure rates between 7.5 and 15% are recommended, reflecting a tradeoff between maintaining bus travel speeds and achieving the higher capacities required in downtown areas. At a 15% failure rate, queues form behind the bus stop for about 10 minute out of the hour, and simulation indicates that bus speeds at capacity are about 20% lower than when scheduled bus volumes are well below capacity
Outside downtown areas, a design failure rate of 2.5% is recommended whenever possible, particularly when off-line stops are provided, as queues will block a travel lane whenever a bus stop failure occurs. However, failure rates up to 7.5% can be accepted.
Although the failure rate is typically set as a design value, it can also be measured in the field when evaluating bus capacity under existing conditions.
Source: TCQSM 6-63 – 6-64

## Slide 19: Step 4 – Determine Dwell Time
Three dwell time estimation methods:
  Field measurements
    Recommended whenever possible
  Default values
    Provides conservative estimate of the critical dwell time
  Calculation
    Good for estimating changes in dwell time
Step 1: Define the Facility
Step 3: Set a Design Bus Stop Failure Rate
Step 2: Gather Input Data
Step 4: Determine Dwell Time
Step 5: Determine Loading Area Capacity
Step 6: Determine Bus Stop Capacity
Step 7: Determine Facility Bus Capacity
Step 8: Determine Facility Person Capacity
Final bus stop on facility?
No
Yes
Notes: There are several methods that you might use to estimate dwell time, depending on where you are in the process of service planning or operations.
Source: National Transit Institute, “Transit Capacity and Quality of Service Course,” 2003.

## Slide 20: Step 4 – Determine Dwell Time
Dwell Time – Calculation
  Average passenger service times for each bus door channel and movement
Notes: When a mix of fare payment options are provided use the information from Step 2 to create a weighted average service time based on the mix of fare media used.
The base values are for level boarding with no standees on the bus; add 0.5 s/p to boarding times for standees and add 0.5s/p for non-level boarding (1.o s/p for motor coaches). In addition, if more than 25% of the passenger flow through a single door is in the opposite direction of the main flow of passengers, increase both boarding and alighting times by 20% to account for passenger congestion at the door.
Source: TCQSM 3rd Edition 6-7, 6-68

## Slide 21: Step 4 – Determine Dwell Time
Other Dwell Time Considerations
  Wheelchair loading & securement
    Typical lift times: 60-200 sec
    Low-floor bus ramps: 30-60 sec
    Range reflects skill and familiarity of user
  Bicycle rack loading and unloading
    20-30 sec
  Timepoint holding
Notes: Wheelchair times are in addition to any other passengers service times. Bike loading/unloading may or may not increase dwell time, depending on how many other passengers board/alight while the bike is being loaded/unloaded.
These times are good to be aware of, but you generally wouldn’t account for them unless they were regular events at a stop (occasional events covered by dwell time variability)

## Slide 22: Step 5 – Determine Loading Area Capacity
Step 1: Define the Facility
Step 3: Set a Design Bus Stop Failure Rate
Step 2: Gather Input Data
Step 4: Determine Dwell Time
Step 5: Determine Loading Area Capacity
Step 6: Determine Bus Stop Capacity
Step 7: Determine Facility Bus Capacity
Step 8: Determine Facility Person Capacity
Final bus stop on facility?
No
Yes
Bus capacity of loading area dependent on:
  Dwell time
    From Step 4
  Operating margin
  Clearance time
  Traffic signal time
Notes: The sum of dwell time and clearance time equals the average time a given bus occupies a loading area.
The operating margin accounts for longer-than-average dwells to ensure that most buses will be able to immediately use the loading area upon arriving.

## Slide 23: Step 5 – Operating Margin
Failure rate used with dwell time variability and average dwell time to provide operating margin
Operating margin is the maximum amount of time that an individual bus dwell time can exceed the average without causing failure for the next buses scheduled to use the stop
Notes: The failure rate (step 3) is used in combination with dwell time variability and the average dwell time (both discussed in Step 4) to provide an operating margin, the maximum amount of time that an individual bus dwell time can exceed the average dwell time without creating the likelihood of a bus stop failure, when the number of buses scheduled to use the stop approaches the stop's capacity.
Because the real-world dwell times will vary from the average, some failure will always be a statistical possibility. Operating margin is partly a matter of agency policy, depending on how much bus stop failure will be tolerated.
The lower the design failure rate, the greater the operating margin and schedule reliability, and the lower the loading area capacity. Conversely, the greater the design failure rate, the lower the operating margin and schedule reliability, but the greater the loading area capacity.
The sum of dwell time, clearance time, and operating margin gives the minimum headway between buses needed to limit bus stop failure to the design level, for a bus stop consisting of one loading area. (Multiple loading areas will be addressed in Step 6.)
Dividing this headway into 3,600 s/h produces the loading area capacity, the number of buses per hour that can use a single loading area at a bus stop at the design failure rate.
Briefly explain the variables in the operating margin equation. However, do not emphasize this.

## Slide 24: Step 5 – Determine Loading Area Capacity
Clearance Time Values
  Start up and exit time = 10 seconds
  For “off-line” stops (out of traffic flow), add re-entry delay
    Depends on curb-lane volumes
    Depends on yield-to-bus laws and motorist compliance
    Nearby signals will affect
Notes: Clearance time for on-line stops is very simple: Just 10 seconds to accelerate out of the stop.
Clearance time for off-line stops is more complicated because in addition to the time the bus takes to accelerate the bus must also merge into traffic (reentry delay). The time this takes will depend on traffic volumes and signal timing. For more details on this calculation see TCQSM 3rd Edition 6-71- 6-76

## Slide 25: Step 5 – Determine Loading Area Capacity
Traffic Signal Time
  At near-side stops buses may not be able to leave the loading area immediately after serving passengers
  At far-side stops buses may not be able to immediately enter the stop
  In both cases the portion of time that the traffic signal permits bus movement is given by the g/C ratio
Notes: The g/C ratio is the ratio of the time the signal is effectively green for buses to the overall length of the traffic signal cycle. Multiplying the g/C ratio by 3,600 gives the number of seconds in an hour that buses are free to enter or leave the stop.

## Slide 26: Step 6 – Bus Stop Capacity
Determine the number of effective loading areas
Adjust capacity for traffic blockage at traffic signals
Calculate bus stop capacity
Step 1: Define the Facility
Step 3: Set a Design Bus Stop Failure Rate
Step 2: Gather Input Data
Step 4: Determine Dwell Time
Step 5: Determine Loading Area Capacity
Step 6: Determine Bus Stop Capacity
Step 7: Determine Facility Bus Capacity
Step 8: Determine Facility Person Capacity
Final bus stop on facility?
No
Yes
Notes: Instructor: Overview slide. Each step is explained in next slides. Mention and move on.

## Slide 27: Step 6 – Bus Stop Capacity
Step 6a: Determine the number of effective loading areas
  Stops with multiple loading areas in linear sequence have a lower number of effective loading areas than the total
  Non-linear stops are 100% efficient
Notes: The majority of on-street bus stops use linear loading areas. Depending on how closely buses stop near to each other in adjacent linear loading areas, buses may be able to exit loading areas independently; however, in constrained situations, they need to wait for the bus(es) in front of them to depart before they can depart. Furthermore, upon entering a bus stop consisting of multiple loading areas, a bus will stop at the forward-most available stop. If another bus is occupying one of the stop's loading areas, the arriving bus will need to stop behind it, potentially leaving loading areas farther ahead unoccupied because they cannot be accessed at that point in time.
Because buses can temporarily block loading areas from other buses, there is a diminishing-returns effect when using additional linear loading areas to add capacity to a bus stop. The more loading areas that are added, the more likely that some of them will be inaccessible at a given point in time. The concept of effective loading areas is used to describe this effect, where the second linear loading area provides less capacity than the first, the third adds even less, and so on.

## Slide 28: Step 6 – Bus Stop Capacity
Step 6b: Adjust capacity for traffic blockage at traffic signals
  Conflicting vehicle movements
  Conflicting pedestrian movements
Notes: Conflicting vehicle and pedestrian movements may use up signal green time that otherwise would be available for bus movements. The impact on bus stop capacity depends on:
the movement's traffic volume relative to its capacity,
the bus stop location (e.g., near side, far side), and
the ability or inability of buses to move around turning vehicles.
If other vehicles are not allowed to use the bus facility (e.g., a busway, a freeway managed lane, an exclusive bus lane that does not allow general traffic to turn from the lane), there is no traffic blockage impact on capacity and this step can be skipped. Similarly, if the stop in question is located more than one-half block away from a traffic signal, and outside the influence of a queue of stopped vehicles generated by the signal, this step can be skipped.

## Slide 29: Step 6 – Bus Stop Capacity
Step 6c: Calculate bus stop capacity
Notes: Bus stop capacity is the capacity of a single loading area multiplied by the number of effective loading areas and the traffic blockage adjustment factor.

## Slide 30: Step 7: Facility Bus Capacity
Capacity is calculated for three different types of facility:
  Non-stop facility capacity
  Facility capacity withoutskip-stop operation
  Facility capacity with skip-stop operation
For b and c there is also a further step:
  Check v/c ratios of all stops along the facility
Step 1: Define the Facility
Step 3: Set a Design Bus Stop Failure Rate
Step 2: Gather Input Data
Step 4: Determine Dwell Time
Step 5: Determine Loading Area Capacity
Step 6: Determine Bus Stop Capacity
Step 7: Determine Facility Bus Capacity
Step 8: Determine Facility Person Capacity
Final bus stop on facility?
No
Yes

## Slide 31: Step 7: Facility Bus Capacity
Step 7a: Non-stop facility capacity
  Determine capacity of both the facility itself and of terminals serving it
Notes: For example, the Lincoln Tunnel bus lane operates as a non-stop facility, the capacity of which is determined by the Port Authority Bus Terminal. Up to 735 buses per hour operate on the New Jersey approach to the Lincoln Tunnel.
Potential constraints in this case include:
A busway station where a passing lane is not provided
Facility capacity used by other vehicles
A low-capacity intersection located before or after the facility being analyzed
The combined bus capacity of the terminal(s), transit center(s) and/ or streets that buses on the non-stop facility end up.
Sources:
TCQSM 3rd Edition 6-80
http://www.transportpolicy.org.uk/PublicTransport/LincolnTunnel/LincolnTunnel.htm

## Slide 32: Step 7: Facility Bus Capacity
Step 7b: Facility capacity without skip-stop operation:
  Facility capacity is equal to the capacity of the critical stop along the facility
  When all buses use all stops this is the stop with the lowest capacity
  With a mix of services (e.g. local and limited stop) this is the stop used by all service types that has the lowest capacity

## Slide 33: Step 7: Facility Bus Capacity
Step 7c: Facility capacity with skip-stop operation:
  Facility capacity depends on three factors:
    The capacities of the critical bus stops of each skip-stop group
    Arrival patterns of the buses (random arrivals/typical arrivals/platooned arrivals)
    Vehicle traffic volume in the adjacent lane
  See TCQSM Chapter 6 for more details
Notes: When skip-stop operation is used, the bus facility capacity is equal to the sum of the capacities of the critical bus stops of each skip-stop group, multiplied by an adjustment factor fk reflecting inefficient arrival patterns and the effects of high vehicular traffic volumes in the adjacent lane:
where
with
where
and with
where
A planning-level estimate of the adjacent lane capacity can be made by multiplying the typical downtown lane vehicle saturation flow rate of 1,7 50 vehicles per lane per hour of green by the g/C ratio of the bus lane. Outside the downtown area, a saturation
flow rate of 1,600 vehicles per lane per hour of green may be used. Consult the Highway Capacity Manual if a more detailed estimate of adjacent lane capacity is required.
The values provided by the equations above result in added capacity with skip-stop operation, even when the adjacent lane is fully utilized by other vehicles, since non-stopping buses have zero dwell time at the stop. When there is no spreading of stops, there is no increase in capacity rendered by the adjacent lane, as all buses must stop at every stop.
TCQSM 3rd Edition 6-82
When skip-stop operation is used, the bus facility capacity is equal to the sum of the capacities of the critical bus stops of each skip-stop group, multiplied by an adjustment factor fk reflecting inefficient arrival patterns and the effects of high vehicular traffic volumes in the adjacent lane:
𝐵= 𝑓_𝑘 (𝐵_1+ 𝐵_2+ …+ 𝐵_𝑛 )
where
(TCQSM 6-82)
A planning-level estimate of the adjacent lane capacity can be made by multiplying the typical downtown lane vehicle saturation flow rate of 1,750 vehicles per lane per hour of green by the g j C ratio of the bus lane. Outside the downtown area, a saturation flow rate of 1,600 vehicles per lane per hour of green may be used. Consult the Highway Capacity Manual if a more detailed estimate of adjacent lane capacity is required.
The values provided by Equation 6-20 and Equation 6-21 result in added capacity with skip-stop operation, even when the adjacent lane is fully utilized by other vehicles, since non-stopping buses have zero dwell time at the stop. When there is no spreading of stops, there is no increase in capacity rendered by the adjacent lane, as all buses must stop at every stop.

## Slide 34: Step 7: Facility Bus Capacity
Step 7d: Check v/c ratios of all stops along the facility
  If volume exceeds capacity, buses will wait behind stop, resulting in:
    Poor bus speeds
    Schedule reliability problems
    Potential traffic operations issues
Notes: Even when the critical bus stop provides sufficient capacity for the scheduled or planned number of buses using the facility, other bus stops may not provide sufficient capacity to serve even the reduced number of buses using those stops. Therefore, the scheduled or planned volume of buses at each bus stop should be compared to the stop's capacity. If the volume exceeds the capacity, buses will queue behind the stop, resulting in poor bus speeds, schedule reliability problems, and potential traffic operations issues.
TCQSM 3rd Edition 6-83

## Slide 35: Steps 5-7: Concentrated Bus Arrivals
Steps 5-7 determine hourly capacities
If bus arrivals are more concentrated during a particular portion of the hour, volumes should be checked for the peak-of-the-peak period
Notes: The capacities determined in Steps 5-7 are hourly capacities that assume that bus arrivals are spread out over the course of the hour. If bus arrivals are more concentrated during a particular portion of the hour (e.g., peaking over a 15-or 30-min period), volumes and capacities should also be checked during those peak-of-the-peak periods. For example, dividing the hourly capacity by 4 gives the maximum number of buses a loading area, bus stop, or facility can accommodate in a given 15-min period.
Transit Capacity and Quality of Service Manual, 3rd Edition ; Chapter 6, page 6-84

## Slide 36: Step 8: Facility Person Capacity
Once vehicle capacity is known, person capacity is relatively simple to determine
Person capacity is influenced by:
  The facility’s bus capacity
  Transit agency policy regarding passenger loads
  Scheduled headways
  Passenger demand diversity
Step 1: Define the Facility
Step 3: Set a Design Bus Stop Failure Rate
Step 2: Gather Input Data
Step 4: Determine Dwell Time
Step 5: Determine Loading Area Capacity
Step 6: Determine Bus Stop Capacity
Step 7: Determine Facility Bus Capacity
Step 8: Determine Facility Person Capacity
Final bus stop on facility?
No
Yes

## Slide 37: Step 8: Facility Person Capacity
Vehicle Capacity
  A stop or facility’s vehicle capacity sets an upper limit on the number of passengers that could be carried during a given time
  Bus width
    Wider bus provides more standing area
  Seating configuration
    More comfortable seating arrangement vs. greater passenger capacity vs. better accessibility (e.g., low-floor buses)
Notes: First let’s discuss the capacity of the vehicle itself. The vehicle width will obviously affect the amount of space, as will the design of the seating configuration. In addition, high-floor buses have greater passenger capacity than low-floor buses due to avoiding the obstruction of wheel wells.
Capacity will be lower when standees not allowed. It may also be necessary to provide a safety margin of unused capacity so that passengers aren’t left waiting for the next bus if the bus has more passengers than usual.

## Slide 38: Step 8: Facility Person Capacity
Vehicle Capacity
Source: TCRP, Transit Capacity and Quality of Service Manual. 2013.
Notes: Here are some sample values for different vehicle types.

## Slide 39: Step 8: Facility Person Capacity
Operator Policy Factors
  Loading policies
    Standees allowed?
    Crush loading?
    Maximum schedule load
      Average over the hour, or not to be exceeded during the hour?
Notes: Capacity will be lower when standees not allowed. The agency may also need to provide a safety margin of unused capacity so that passengers aren’t left waiting for the next bus if the bus has more passengers than usual.
Maximum schedule load is synonymous with “capacity,” assuming a reasonable number of standees. It represents the upper limit for scheduling purposes. Maximum schedule loads are typically 125 to 150% of a bus’s seating capacity, for example 54 to 64 passengers on a typical 40-foot (12-meter) bus.
Maximum schedule load is synonymous with “capacity,” assuming a reasonable number of standees. It represents the upper limit for scheduling purposes. Maximum schedule loads are typically 125 to 150% of a bus’s seating capacity, for example 54 to 64 passengers on a typical 40-foot (12-meter) bus. Therefore, crush loads should not be used for transit capacity calculations.
Image:
http://www.flickr.com/photos/safetyguy1656/4533351126/

## Slide 40: Step 8: Facility Person Capacity
Passenger Loading Preferences
  Passengers in smaller cities less likely to tolerate high levels of crowding
    May choose to wait for the next bus, even if some standing space is available
    Passengers more likely to wait when they know how long the wait will be, and the wait is relatively short

## Slide 41: Step 8: Facility Person Capacity
Passenger Demand Diversity
  Passengers will typically not arrive at a stop at an even rate
  Need sufficient capacity to handle peaks in demand without causing pass-ups
  Not all of the available capacity (seats and standing space) will be utilized because of variations in passenger arrivals
Notes: Travelers do not typically arrive at a bus stop at an even rate – they often come in groups or peak at certain times.
As a result, capacity needs to serve a peak ridership that may only occur for a brief period of time.

## Slide 42: Person Capacity & Quality of Service
Person capacity and quality of service are related
Improving one may improve or reduce the other
  Increasing service frequency
  Using buses with fewer seats, more standing area
Notes: Capacity will be lower when standees not allowed. May also need to provide a safety margin of unused capacity so that passengers aren’t left waiting for the next bus if the bus has more passengers than usual.
Image:
http://www.flickr.com/photos/benchilada/2467374335/

## Slide 43: Bus Speed Calculation Process
Step 1: Define the Facility
Step 3: Determine Section Maximum Capacity
Step 2: Gather Input Data
Step 4: Determine Base Bus Running Time Rate
Step 5: Adjust for Skip-Stop Operation
Step 6: Adjust for Bus Congestion
Step 8: Determine Average Facility Speed
Final section on facility?
No
Yes
Step 7: Determine Average Section Speed
Notes: The bus speed calculation process has eight main steps. This parallels the bus capacity calculation process.

## Slide 44: Step 1: Define The Facility
Defined the same way as for Bus Capacity
  Once defined, it is divided into sections with similar right-of-way types
  Average speed calculated first for each individual section, then combined into the overall facility speed
  Sections should be at least 0.25 mi (400 m) and preferably 0.5 mi (800 m) long.
Step 1: Define the Facility
Step 3: Determine Section Maximum Capacity
Step 2: Gather Input Data
Step 4: Determine Base Bus Running Time Rate
Step 5: Adjust for Skip-Stop Operation
Step 6: Adjust for Bus Congestion
Step 8: Determine Average Facility Speed
Final section on facility?
No
Yes
Step 7: Determine Average Section Speed
Notes: Transit Capacity and Quality of Service Manual, 3rd Edition , Chapter 6, page 6-87

## Slide 45: Step 2: Gather Input Data
Input data for calculating bus capacity required
The following data are required for each section of the facility:
  Average stop spacing
  Average dwell time
  Scheduled number of buses at the critical stop(s)
  Traffic signal timing and spacing
  Traffic interference
Step 1: Define the Facility
Step 3: Determine Section Maximum Capacity
Step 2: Gather Input Data
Step 4: Determine Base Bus Running Time Rate
Step 5: Adjust for Skip-Stop Operation
Step 6: Adjust for Bus Congestion
Step 8: Determine Average Facility Speed
Final section on facility?
No
Yes
Step 7: Determine Average Section Speed
Notes: The following data are required for each section of the facility:
Average stop spacing (stop/mi, stop/km)
Average dwell time (s/bus/stop)
Scheduled number of buses at the critical stop (s) (bus/h)
Traffic signal timing and spacing (typical, signals set for bus progression, signals more frequent than bus stops)
Traffic interference (general traffic prohibited, bus lane with right-turn lanes, bus lane with traffic/parking blockage, mixed traffic).

## Slide 46: Step 3: Section Maximum Capacity
Apply the bus capacity methodology with the following adjustments:
  Each section should be treated as its own facility
  A 25% failure rate should be used to estimate maximum capacity
Step 1: Define the Facility
Step 3: Determine Section Maximum Capacity
Step 2: Gather Input Data
Step 4: Determine Base Bus Running Time Rate
Step 5: Adjust for Skip-Stop Operation
Step 6: Adjust for Bus Congestion
Step 8: Determine Average Facility Speed
Final section on facility?
No
Yes
Step 7: Determine Average Section Speed

## Slide 47: Step 4: Base Bus Running Time Rate
Step 4 estimates a travel time rate in minutes per mile based on the bus’s running speed between stops, stop spacing, and delays due to traffic interference
Base Bus Running Time Rate
Unimpeded Bus Running Time Rate
Additional Running Time Losses
=
+
Step 1: Define the Facility
Step 3: Determine Section Maximum Capacity
Step 2: Gather Input Data
Step 4: Determine Base Bus Running Time Rate
Step 5: Adjust for Skip-Stop Operation
Step 6: Adjust for Bus Congestion
Step 8: Determine Average Facility Speed
Final section on facility?
No
Yes
Step 7: Determine Average Section Speed

## Slide 48: Step 4a: Unimpeded Bus Running Rate
The unimpeded travel time rate incorporates:
  Average dwell time of all bus stops in the section
  Acceleration and deceleration delays for each stop
  Time spent running at the bus’s running speed for the facility

## Slide 49: Step 4a: Unimpeded Running Time Rate
Illustrative Values
(CBD)
Notes: Calculated using the method given in TCQSM

## Slide 50: Step 4c: Base Running Time Rate
Calculate base bus running time
  The sum of the unimpeded running time and the additional running time losses
Notes: Source: TCQSM 6-90

## Slide 51: Step 5: Adjust for Skip-Stop Operation
Bus
Bus
Bus
400 ft
Step 1: Define the Facility
Step 3: Determine Section Maximum Capacity
Step 2: Gather Input Data
Step 4: Determine Base Bus Running Time Rate
Step 5: Adjust for Skip-Stop Operation
Step 6: Adjust for Bus Congestion
Step 8: Determine Average Facility Speed
Final section on facility?
No
Yes
Step 7: Determine Average Section Speed
Notes: Source: TCQSM 6-90

## Slide 52: Step 5: Skip-Stop Operation
Longer distance between stops allows a higher speed
This will be offset by increased dwell time, as each stop accommodates more passengers
Bus
Bus
800 ft
Notes: Skip-stop operation spreads buses out among a series of bus stops, allowing for an increase in speeds. The analytical procedure accounts for the skip-stop operations by considering only the bus stops in the skip-stop pattern. For example, if bus stops are located 400ft (125m) apart (say a stop at each intersection), a two-block skip-stop pattern provides 800ft (250m) between stops for a bus using that pattern. A bus with a two-block stop pattern would be able to proceed faster than a bus with a one-block stop pattern. However, some of this increase will be offset by increases in dwell times, as each stop will have to accommodate more passengers.
The ability of buses to leave the curb lane to pass stopped vehicles is another factor in the ability to attain an increase in speed. This ability depends on the availability of an adjacent lane or the provision of an off-line bus stop. Where dual bus lanes or off-line bus stops are provided, the anticipated bus speed can be calculated using the distance between the bus stops served. Where congestion in the adjacent lane results in essentially no passing-lane availability, the buses will progress as if they were stopping I at each stop with a zero dwell time at the intermediate stops. When partial use of the adjacent lane is available, the bus speed will be somewhere in between.
Source: TCQSM 6-90

## Slide 53: Step 6: Adjust for Bus Congestion
As the number of buses using a lane increases, there is a greater probability that one bus will delay another
Step 1: Define the Facility
Step 3: Determine Section Maximum Capacity
Step 2: Gather Input Data
Step 4: Determine Base Bus Running Time Rate
Step 5: Adjust for Skip-Stop Operation
Step 6: Adjust for Bus Congestion
Step 8: Determine Average Facility Speed
Final section on facility?
No
Yes
Step 7: Determine Average Section Speed
Notes: This table illustrated the effects of increasing bus volumes on bus speeds. There is no effect on bus speeds until one-half of the bus lane's maximum bus capacity is in use. As scheduled bus volumes increase further, bus speeds begin to drop as buses interfere with the ability of each other to enter and exit bus stops and to pass. When a bus lane's maximum capacity is scheduled, achievable speeds are approximately half of what they could be at lower bus scheduled volumes.
Source: TCQSM 6-93

## Slide 54: Step 7: Determine Average Section Speed
The base bus running time rate is divided by the skip-stop operation and bus-bus interference factors to produce the overall section running time rate
This can be converted into a speed by dividing 60 by this number
Step 1: Define the Facility
Step 3: Determine Section Maximum Capacity
Step 2: Gather Input Data
Step 4: Determine Base Bus Running Time Rate
Step 5: Adjust for Skip-Stop Operation
Step 6: Adjust for Bus Congestion
Step 8: Determine Average Facility Speed
Final section on facility?
No
Yes
Step 7: Determine Average Section Speed

## Slide 55: Step 8: Determine Average Facility Speed
The travel time rates for each section are multiplied by the respective section lengths and then summed to produce a total travel time for the facility
The average facility speed is the facility length divided by the facility travel time
Step 1: Define the Facility
Step 3: Determine Section Maximum Capacity
Step 2: Gather Input Data
Step 4: Determine Base Bus Running Time Rate
Step 5: Adjust for Skip-Stop Operation
Step 6: Adjust for Bus Congestion
Step 8: Determine Average Facility Speed
Final section on facility?
No
Yes
Step 7: Determine Average Section Speed