## Slide 1: Module 4, Lesson 3
Route Level Planning and Design Concepts

## Slide 2: Learning Objectives
Describe scheduling concepts that impact running time
Express the basic principles and usage of ridership projections
Examine route level resource allocation and constraints

## Slide 3: Fundamentals of Transit Running Time

## Slide 4: A Day in the Life of a Bus
Block – the daily assignments of a single bus
Run – the daily assignments of a single driver
Trip – the one-way operation between two terminal points on a route
Notes: This module will start by summarizing the different events that a bus goes though in a day of operations (or a “block”). Understanding each of these events is crucial to scheduling bus service.
First it is important to understand the terminology:
Block - A vehicle schedule, the daily assignment for an individual bus. One or more runs can work a block. A driver schedule is known as a "run."
Run - A driver's daily work assignment. One or more runs can work a single block. Runs can also work on multiple blocks. A driver's schedule is primarily determined for each sign-up period through the run-cut process where bus schedules are integrated with driver assignments.
Trip - The one-way operation of a revenue vehicle between two terminal points on a route. Trips are generally noted as inbound, outbound, eastbound, westbound, etc. to identify directionality when being discussed or printed.
Sources:
http://www1.honolulu.gov/dts/transit_glossary.htm
http://www.flickr.com/photos/zigzaglens/3092836403/

## Slide 5: Start from the Garage
Deadhead is non-revenue travel:
  From the garage to the start of the route
  From the end of the route back to the garage
  From the end of one route to the start of another
Notes: The bus starts in the garage and must travel to the starting point of its route. This travel before going into revenue service is called deadhead.
There are three types of deadhead or non-revenue bus travel time:
Bus travel from the garage to the terminus point where revenue service begins
Bus travel to the garage from a terminus point where revenue service ends
Travel between the end of service on one route to the beginning of another
Transit service planners should attempt to minimize deadhead, as it represents wasted resources.
Some agencies have been able to make the most out of deadhead by leaving their vehicles in service during this period.
Sources:
http://www1.honolulu.gov/dts/transit_glossary.htm
http://www.flickr.com/photos/rossendalewadey/2855149715/

## Slide 6: Travel Speed Topics
Travel time and speed factors
  Running speed
  Flow interruptions
  Stopping patterns
Bus travel speed estimation
Why is travel time important to transit agencies? To transit users?
Notes: As a bus travels along its route, several factors will affect its overall travel speed and the time of travel. Most obvious is its unencumbered running speed – but in reality, it will also have to contend with interruptions in the traffic flow and the delay produced at each bus stop. First we will discuss each of these factors that affect travel speeds, and then we will touch on some methods of estimating travel speeds.
Source: National Transit Institute, “Transit Capacity and Quality of Service Course,” 2003.

## Slide 7: Some Types of Speed
Travel – “from A to B”
Running – when in motion; sometimes “when in full motion”
Spot – at one instant; e.g. measured by radar
Average – of spot speeds of many vehicles; also average running speed of one vehicle
Notes: We will focus on travel and running speeds in this course.
Travel speed is the overall speed the bus travels at between one point and another – including all stops and delays it encounters.
Running speed does not account for delays – it is only the speed while the bus is moving normally through its route. Running speed is usually much faster than travel speed.
You might also measure the speed of a vehicle at a particular spot or instant, or perhaps average your speed measurements over multiple spots or multiple vehicles.
Source: National Transit Institute, “Transit Capacity and Quality of Service Course,” 2003.

## Slide 8: Running Speed Factors
Running speed depends on:
  Bus vehicle performance
  Roadway design
  Traffic volume and congestion on facility
    Depends on location – slower downtown
    Depends on time – slower during rush hour
Notes: Remember, running speed is the speed when the bus is in motion; sometimes “when in full motion.”
It is influenced by a number of factors. One is the vehicle itself: How quickly can it accelerate? How well can it keep up with traffic?
Another is the roadway design: Narrow streets or sharp bends in the road force a bus to slow down. If the road has potholes or is poorly maintained, this slows travel as well.
A third factor is the current usage of the roadway. If it is a congested urban location – or if your vehicle is traveling during rush hour – you should expect traffic to move at a slower speed and plan accordingly.
Time savings based on speed has a varying significance based on how long the trip in question is. The time savings going from, say, 50 mph to 60 mph running speeds, may not always be particularly significant, but will entail added fuel costs and may decrease passenger comfort.
Example: travel distance on transit, say, 5 miles.
At 50 mph => 1/10th of an hour, i.e., 6 minutes.
At 60 mph => 1/12th of an hour, i.e., 5 minutes.
Savings: 1 minute. Is it noticeable by the customer?
For a trip of 50 miles
At 50 mph => TT=60 minutes
At 60 mph => TT=50 minutes. That would be noticed.
Source: National Transit Institute, “Transit Capacity and Quality of Service Course,” 2003.
Image sources: http://www.sfcta.org/van-ness-avenue-bus-rapid-transit-about

## Slide 9: Interrupted Flow
Vehicles often experience interruptions:
  Traffic signal timing and spacing
  Is there an exclusive bus lane? Is it enforced?
Notes: And interruption in bus traffic will slow down the overall running speed. Common interruptions include traffic signals and delays from other vehicles.
These factors mainly apply to arterial street bus lanes and mixed traffic situations.
Sources: National Transit Institute, “Transit Capacity and Quality of Service Course,” 2003.
http://www.flickr.com/photos/gphemsley/4650797847/, http://www.streetsblog.org/2010/03/24/state-senate-stands-in-the-way-of-better-enforcement-for-new-bus-lanes/

## Slide 10: Traffic Signal Timing
If buses must wait for a green light after all passengers have been served, fewer buses can use the stop during a given time
Capacity reduction is related to the g/C ratio – the length of the green interval for the bus’ direction, divided by the signal’s cycle length
Green | 30 sec | 60
Yellow | 3 | 3
All Red | 2 | 2
Example:
Notes: The effects of traffic signals are typically described in terms of the g/C ratio. This is the ratio of the green interval time in the bus’ direction to the signal’s whole cycle length.
For example: If an intersection approach has a green signal for 30 seconds out of a 100-second cycle length, the g/C ratio is 0.3. Or in the other direction, a green signal for 60 seconds out of a 100-second cycle gives a g/C ratio of 0.6.
Source: National Transit Institute, “Transit Capacity and Quality of Service Course,” 2003.

## Slide 11: Stopping Patterns
All transit types are affected by:
  Stop spacing and location
  Average dwell time
Increasing stop spacing; decreasing dwell times improves travel speeds
Notes: All transit vehicles experience some delay from making their stops. The amount of stopping delay depends on a number of factors, including how closely the stops are spaced and how much time is spend loading and unloading passengers.
Source: National Transit Institute, “Transit Capacity and Quality of Service Course,” 2003.

## Slide 12: Typical Bus Stop Spacing
Environment | Spacing range | Typical spacing
Central core areas of CBDs | 300 to 1000 ft | 600 ft
Urban areas | 500 to 1200 ft | 750 ft
Suburban areas | 600 to 2500 ft | 1000 ft
Rural areas | 650 to 2640 ft | 1250 ft
Notes: With this understanding of how stopping patterns influence speed, how should service planners weigh the tradeoff between serving more stops and providing faster service? In large part it depends upon the environment where the bus is running. Typical stop spacing varies greatly with the density of the land use context.
Source:
R.K. Brail/P.J. Larrousse, Rutgers University

## Slide 13: Travel Speed Summary
Increasing travel speeds improves transit competitiveness and efficiency
Dwell time and stop spacing are important speed factors for all bus facilities
Signal timing and traffic congestion are also important factors for interrupted-flow facilities
Consider trade-offs: Actions to improve capacity may have speed and quality of service implications
Notes: Source: National Transit Institute, “Transit Capacity and Quality of Service Course,” 2003.

## Slide 14: Dwell Time
Albuquerque, New Mexico
Notes: (Image animates automatically.)
The time a transit vehicle spends at a stop is called “dwell time,” and it has a considerable impact on total travel time. Let’s take a closer look at what dwell time entails.
Source: National Transit Institute, “Transit Capacity and Quality of Service Course,” 2003.

## Slide 15: Dwell Time
Three main components of dwell time:
  Door open and close time, and time waiting to depart once the doors close
  Passenger flow time
  Time the doors remain open after passenger flow ceases
Dwell time is frequently dominant factor in determining the minimum headway and line capacity
The stop with the highest passenger volume (the “critical stop”) often controls line capacity
Notes: Explain the three main components of dwell time:
  Door open and close time, and time waiting to depart once the doors close
  Passenger flow time – boarding and alighting
  Time the doors remain open after passenger flow ceases
Dwell time can be a crucial factor in the overall operation of a route. The stop with the greatest dwell time will set the limit on the capacity of the entire route.
Source:
R.K. Brail/P.J. Larrousse, Rutgers University

## Slide 16: Dwell Time Factors
Dwell time is directly related to the passenger demand at a stop
Reducing dwell time typically involves reducing the time to serve boarding & alighting passengers
Passenger
Demand
On-Board
Circulation
Fare Payment
Method
Vehicle
Type/Size
Bus Stop
Spacing
Door Open/
Close Time
Notes: Most obviously, dwell time is related to passenger demand – each passenger boarding or alighting will take a certain amount of time.
Source: National Transit Institute, “Transit Capacity and Quality of Service Course,” 2003.

## Slide 17: Dwell Time Factors
Simplifying fare payment reduces service time for boarding passengers
  Tickets, tokens, passes
  Pre-paid fares, pay-on-exit
  Smart cards
Passenger
Demand
Fare Payment
Method
On-Board
Circulation
Vehicle
Type/Size
Bus Stop
Spacing
Door Open/
Close Time
Notes: Reducing the time required to serve individual passengers reduces the time to serve all passengers and, thus, reduces dwell time. For example, pay-on-exit allows passengers to use all doors to board at the busiest stops, and spreads out the time required to pay fares over the entire route. Pay-on-exit can also be used to control simple zone-based fare systems.
Source: National Transit Institute, “Transit Capacity and Quality of Service Course,” 2003.

## Slide 18: Dwell Time Factors
Boarding times increase when passengers are standing in the aisle
Exiting through the front door delays passengers waiting to board
Passenger
Demand
On-Board
Circulation
Fare Payment
Method
Vehicle
Type/Size
Bus Stop
Spacing
Door Open/
Close Time
Notes: This is the reason bus operators ask people to move to the back of the bus. Blocking the entrance creates a longer dwell time.
Also, when passengers exit through a narrow front door, passenger boarding is delayed, which also increases dwell time. When passengers exit via the back door, boarding and alighting can occur simultaneously.
Source: National Transit Institute, “Transit Capacity and Quality of Service Course,” 2003.

## Slide 19: Dwell Time Factors
The number of doors and their width determine how many people can board and alight at the same time
Boarding & alighting times are faster for low-floor buses than high-floor
Passenger
Demand
Vehicle
Type/Size
On-Board
Circulation
Fare Payment
Method
Bus Stop
Spacing
Door Open/
Close Time
Notes: Wider doors can serve more passengers at once – though boarding times will not be affected by the number of doors if passengers have to pay the driver.
Low-floor buses also are faster for boarding, though at the cost of a slightly lowered seating capacity.
Source: National Transit Institute, “Transit Capacity and Quality of Service Course,” 2003.

## Slide 20: Dwell Time Factors
Trade-off: reducing the number of stops vs. increasing walking distances to stops
Reducing boarding volume at the critical stop increases facility’s capacity
Passenger
Demand
On-Board
Circulation
Fare Payment
Method
Vehicle
Type/Size
Bus Stop
Spacing
Door Open/
Close Time
Notes: Again, the fewer passengers to be served, the shorter the dwell time. More stops generally will mean fewer passengers at each.
Source: National Transit Institute, “Transit Capacity and Quality of Service Course,” 2003.

## Slide 21: Dwell Time Factors
Fixed value, ranges from 2 to 5 seconds
Passenger
Demand
On-Board
Circulation
Fare Payment
Method
Vehicle
Type/Size
Bus Stop
Spacing
Door Open/
Close Time
Notes: Source: National Transit Institute, “Transit Capacity and Quality of Service Course,” 2003.

## Slide 22: Other Dwell Time Considerations
Wheelchair loading and securement
Bicycle rack loading and unloading
Timepoint holding (if running ahead of schedule)
These often are infrequent, random events
  Difficult to plan unless it is a regular occurrence
  Addressed by:
    Dwell time variability for capacity purposes
    Recovery time for scheduling purposes
Notes: These factors aren’t typically included in scheduling unless they become a regular occurrence on a route.
Wheelchair times are in addition to any other passengers service times. Bike loading/unloading may or may not increase dwell time, depending on how many other passengers board/alight while the bike is being loaded/unloaded. These times are good to be aware of, but you generally wouldn’t account for them unless they were regular events at a stop (occasional events covered by dwell time variability)
Source: National Transit Institute, “Transit Capacity and Quality of Service Course,” 2003.
Timepoint Holding
Some transit agencies' operating practice is to hold buses at timepoints if they are running ahead of schedule. Holding can significantly increase the time a bus spends stopped at a bus stop, which reduces the stop's capacity; however, this factor is not directly accounted for in the dwell time definition, which only includes time to serve passengers and open and close the bus doors. If many buses have to hold at a stop, consideration should be given to adjusting the schedule to reduce the need to hold. If a relatively small number of buses have to hold, the time spent holding can be treated as additional dwell time for the purposes of calculating dwell time variability. (TCQSM, 3rd edition, Chapter 6, page 6-70

## Slide 23: Dwell Time Variability
Minneapolis, Minnesota
Notes: (Image animates automatically.)
Source: http://www.flickr.com/photos/northernspark/5932100256/
http://www.flickr.com/photos/northernspark/5932099040/
http://www.flickr.com/photos/northernspark/5931545725/

## Slide 24: Dwell Time Variability
Some buses will dwell longer than the average
Capacity will be lower than if all buses dwelled the same amount of time
This variability is measured by the coefficient of variation of dwell times (cv)
  cv = Standard deviation
  Average
Typical range from 40% to 80% (60% default)
Notes: Ask: Why would it matter how much variation there is in the dwell time?
  It affects the consistency in adhering to the schedule.
  As dwell times become more variable, fewer buses can use the stop without causing following buses to have to wait in the street before entering the stop.
For these reasons, we measure a coefficient of variation. Calculating the coefficient of variation is done by dividing the standard deviation by the average. One would generally use a spreadsheet to calculate the standard deviation of a series of observations.
To illustrate the concept, here are sample values. Zero variability means the dwell times are all exactly the same. One hundred percent variability would mean very considerable variation. The lower the cv value, the better for schedule adherence.
For planning purposes, we can generally use a default value of 60%.
Source: National Transit Institute, “Transit Capacity and Quality of Service Course,” 2003.

## Slide 25: Clearance Time
The time it takes a bus to close its doors and depart a stop
  The loading area is not yet available for use by the next bus
Two parts
  Travel own length – Time for a bus to start up and travel its own length, clearing the stop
  Re-entry delay – When a bus stops out of traffic (off-line), it must wait for a suitable gap in traffic
Notes: Clearance time is the time it takes a bus to close its doors and depart a stop after the passenger flows have ended. During clearance time the loading area is not yet available for use by the next bus.
This time includes two components: All buses have to travel their own length to exit the stop. This takes about ten seconds. However, if the stop is off-line, there may also be time spent waiting for traffic so the bus can re-enter the stream. This re-entry delay will depend on the traffic volume in the adjacent lane.
Source:
R.K. Brail/P.J. Larrousse, Rutgers University

## Slide 26: Yield-to-Bus Laws
Portland, Oregon
Denver, Colorado
Notes: One tactic to reduce clearance time and make re-entry into traffic easier is to establish yield-to-bus laws. However, a 2011 study of these laws found no significant effect on yielding behavior in the field. At this time, the best advice is to observe impacts on driver behavior in your particular service area.
Source:
Huaguo Zhou, Stephanie Bromfield, and Pei-Sung Lin. “An Overview of Yield-to-Bus Programs in Florida.” Journal of Public Transportation, Vol. 14, No. 2, 2011
Images: http://www.ecgi.net/transport-bus.htm, http://denver.cbslocal.com/2011/01/27/yield-to-bus-lights-on-rtd-buses-designed-to-improve-safety-on-roads/

## Slide 27: Failure Rate
How often a bus should arrive at a stop only to find all loading areas occupied
Downtown – rate of 7.5% to 15% recommended
Outside downtown – rate of 2.5% recommended
Notes: Failure rate can be observed in the field, or set as a design value. It has considerable effects on the overall operation of a stop.
Typical failure rates will depend on the type of area being served. A higher failure rate is typically expected in urban areas as opposed with non-urban areas.
Source:
R.K. Brail/P.J. Larrousse, Rutgers University

## Slide 28: Operating Margin
Operating margin is the maximum amount of time that an individual bus dwell time can exceed the average without causing failure for the next buses scheduled to use the stop
Notes: Service planners account for bus stop failure by designing with an operating margin: an allowed amount of time that an individual bus dwell time can exceed the average without causing failure for the next buses scheduled to use the stop.
Source: National Transit Institute, “Transit Capacity and Quality of Service Course,” 2003.
R.K. Brail/P.J. Larrousse, Rutgers University

## Slide 29: Trade-Offs…
… Between Failure Rate and Operating Margin
  Lower operating margins increase failure rate
  Lower operating margins increase loading area capacity
  Failure increases as service frequency increases
  Failure increases as stops are more densely spaced
  Lower failure rates improve schedule reliability
Notes: On one hand, a low failure rate is desirable to ensure a reliable schedule. On the other hand, a higher rate around 25% will optimize your capacity. There is a trade-off, and so the appropriate level of failure to design for is a matter of agency policy.
Source:
R.K. Brail/P.J. Larrousse, Rutgers University
TCRP Transit Capacity and Quality of Service Manual 2013

## Slide 30: Layover Every Trip
Two reasons for layover:
  Recover any time lost to ensure the next trip starts on time
  Rest for the operator
Typical range is 10-20% of trip time
Where should the layover take place?
Notes: The final piece of the bus’ daily journey that you should be aware of is the layover.
Layover — Layover time serves two major functions: recovery time for the schedule to ensure on-time departure for the next trip and, in some systems, operator rest or break time between trips. Layover time is often determined by labor agreement, requiring "off-duty" time after a certain amount of driving time.
Recovery Time — Recovery time is distinct from layover, although they are usually combined together. Recovery time is a planned time allowance between the arrival time of a just completed trip and the departure time of the next trip in order to allow the route to return to schedule if traffic, loading, or other conditions have made the trip arrive late. Recovery time is considered as reserve running time and typically, the operator will remain on duty during the recovery period.
Discuss where the best locations may be to have layover time – e.g. major stops, out of traffic, with a bathroom available, perhaps somewhere to buy a snack.
Image:
http://www.flickr.com/photos/hine/112239782/

## Slide 31: Bus Stop Design

## Slide 32: Locating Bus Stops – Choices
Close stops
Every block to 1/4 mile
Short walk distances
Slower bus trip
Stops farther apart
Every 1/4 mile or more
Longer walk distances
Faster bus trip
Notes: Source:
R.K. Brail/P.J. Larrousse, Rutgers University
Image:
http://www.flickr.com/photos/dnorman/2087167707/

## Slide 33: On-line vs. Off-line Stops
On-line
Off-line
BUS
BUS
Notes: On-line stops: Bus stops in traffic, and can move immediately again after serving passengers (unless blocked by other traffic stopped in front of it).
Off-line stops: Bus stops out of traffic, may need to wait for adjacent lane traffic to clear.
Source: National Transit Institute, “Transit Capacity and Quality of Service Course,” 2003.

## Slide 34: On-street Bus Stop Locations
Notes: Bus stops can also be described by their location relative to an adjacent intersection. The following slides will discuss near-side, mid-block, and far-side bus stops in detail.
Ask the class: Which location do you think is best, and why?
Source:
TCRP Transit Capacity and Quality of Service Manual 2013

## Slide 35: Far-side Locations
Advantages
  Minimizes conflicts between right-turning vehicles and buses
  Provides additional right-turn capacity lane
  Minimizes sight distance problems on intersection approaches
  Encourages pedestrians to cross behind the bus
  Creates shorter deceleration distances for buses
  Allows buses to enter traffic gaps created by signalized intersections
  Facilitates bus signal priority operation
Bus
Notes: Far-side stops may be more appropriate for locations with a heavy right turn volume and a lower through traffic volume. Of course, adjacent land uses and pedestrian flows are also an important part of the decision.
Advantages
  Minimizes conflicts between right-turning vehicles and buses
  Provides additional right-turn capacity by making curb lane available for traffic.
  Minimizes sight distance problems on intersection approaches
  May encourage pedestrians to cross behind the bus, depending on distance from intersection
  Creates shorter deceleration distances for buses, since the intersection can be used to decelerate
  Buses can take advantage of gaps in traffic flow created at signalized intersections
  Facilitates bus signal priority operation, as buses can pass through intersection before stopping
Source:
TCRP Transit Capacity and Quality of Service Manual 2013

## Slide 36: Far-side Locations
Disadvantages
  Could result in traffic queued into intersection when a bus stops in the travel lane
  May obscure sight distance for crossing vehicles
  May increase sight distance problems for crossing pedestrians
  Can cause a bus to stop far side after stopping for a red light, interfering with both bus operations and all other traffic
  May increase the number of rear-end crashes since drivers may not expect buses to stop again after stopping at a red light
Bus
Notes: Far-side stops may be more appropriate for locations with a heavy right turn volume and a lower through traffic volume. Of course, adjacent land uses and pedestrian flows are also an important part of the decision.
Disadvantages
  Could result in traffic queued into intersection when a bus stops in the travel lane
  May obscure sight distance for crossing vehicles
  May increase sight distance problems for crossing pedestrians
  Can cause a bus to stop far side after stopping for a red light, interfering with both bus operations and all other traffic
  May increase the number of rear-end crashes since drivers may not expect buses to stop again after stopping at a red light
Source:
TCRP Transit Capacity and Quality of Service Manual 2013

## Slide 37: Mid-block Locations
Advantages
  Minimizes sight distance problems for vehicles and pedestrians
  May result in passenger waiting areas experiencing less pedestrian congestion
Bus
Notes: Mid-block stops may be beneficial from a traffic flow perspective, but they are inconvenient for pedestrians and encourage jay-walking. These make the most sense at locations where a stop is needed adjacent to a major trip generator.
Advantages
  Minimizes sight distance problems for vehicles and pedestrians
  May result in passenger waiting areas experiencing less pedestrian congestion
Source:
TCRP Transit Capacity and Quality of Service Manual 2013

## Slide 38: Mid-block Locations
Disadvantages
  Requires additional distance for no-parking restrictions
  Encourages passengers to cross street mid-block (jaywalking)
  Increases walking distance for passengers crossing at intersections
Bus
Notes: Mid-block stops may be beneficial from a traffic flow perspective, but they are inconvenient for pedestrians and encourage jay-walking. These make the most sense at locations where a stop is needed adjacent to a major trip generator.
Disadvantages
  Requires additional distance for no-parking restrictions
  Encourages passengers to cross street mid-block (jaywalking)
  Increases walking distance for passengers crossing at intersections
Source:
TCRP Transit Capacity and Quality of Service Manual 2013

## Slide 39: Near-side Locations
Advantages
  Minimizes interferences when traffic is heavy on the far side of the intersection
  Allows passengers to access buses close to crosswalk
  Intersection width available for bus to pull away from the curb
  Eliminates potential for double stopping
  Allows passengers to board and alight while bus stopped for red light
  Allows driver to look for oncoming traffic, including other buses with potential passengers
Bus
Notes: Near-side stops may be more appropriate for locations with a heavy through traffic flow and a lower right turn volume. Of course, adjacent land uses and pedestrian flows are also an important part of the decision.
Advantages
  Minimizes interferences when traffic is heavy on the far side of the intersection
  Allows passengers to access buses close to crosswalk
  Intersection width available for bus to pull away from the curb
  Eliminates potential for double stopping
  Allows passengers to board and alight while bus stopped for red light
  Allows driver to look for oncoming traffic, including other buses with potential passengers
Source:
TCRP Transit Capacity and Quality of Service Manual

## Slide 40: Near-side Locations
Disadvantages
  Conflicts with right-turning vehicles
  Buses obscure curbside traffic control devices and crossing pedestrians
  Sight distance obscured for side street vehicles
  Increases sight distance problems for crossing pedestrians
  Complicates bus signal priority operation,
  Difficulty merging into traffic
Bus
Notes: Near-side stops may be more appropriate for locations with a heavy through traffic flow and a lower right turn volume. Of course, adjacent land uses and pedestrian flows are also an important part of the decision.
Disadvantages
  Increases conflicts with right-turning vehicles
  May result in stopped buses obscuring curbside traffic control devices and crossing pedestrians
  May cause sight distance to be obscured for side street vehicles stopped to the right of the bus
  Increases sight distance problems for crossing pedestrians
  Complicates bus signal priority operation, may reduce effectiveness or require a special queue-jump signal if the stop is located in the parking lane or a right-turn lane
  Potentially more difficult to merge back into traffic at traffic signals due to vehicle queues
Source:
TCRP Transit Capacity and Quality of Service Manual 2013

## Slide 41: Loading Area Designs
Linear
  Typical curb-side stop
  First bus to arrive stops at first loading area
  Buses may be blocked by buses in front
Non-linear
  Buses have assigned stops
  Buses move independently
  More efficient usage
Notes: While linear stop designs are the most common, they are less efficient than non-linear stops because they work on a first-in-first-out principle. The delay of one bus can carry through the line and affect the other buses. The rear loading areas can have longer dwell times, if passengers don’t know where the bus will stop and then need to walk to bus. Buses may also need to wait for bus in front to leave before they can proceed.
Non-linear stops eliminate these issues by allowing each bus to enter and exit independently using assigned stop locations. This is more efficient than a linear stop, but from a design perspective they are harder to implement.
Source: National Transit Institute, “Transit Capacity and Quality of Service Course,” 2003.

## Slide 42: Bus Stop Design Options
Notes: Here are some bus stop design alternatives. The non-linear designs include Sawtooth, Drive-Through, and Angle.
Source:
TCRP Transit Capacity and Quality of Service Manual 2013

## Slide 43: Loading Areas, Stops, and Facilities
L
L
S
F
L = loading area, S = bus stop, F = bus facility
Bus
Bus
L
L
S
Notes: The bus capacity calculation process has three main steps. The capacity of individual loading areas at a bus stop influences the overall bus stop capacity. The critical bus stop capacity influences the bus facility capacity. A “loading area” is a position at a curb where a bus can load and unload passengers. A bus stop will consist of one or more loading areas.

## Slide 44: Bus Stops and Loading Areas
Bus stops may contain multiple loading areas
Linear designs are not 100% efficient
  Loss of efficiency is measured by the number of effective loading areas
Non-linear designs are 100% efficient
Chicago, IL
Notes: Note: The terms “berth” or “bay” are synonymous with “loading area.”
When we discuss bus stop efficiency, we mean how much capacity it gets per each berth. A stop that is “100% efficient” will have the same number of effective loading areas as the number of actual loading areas—doubling the number of loading areas doubles the capacity in these cases.
However, for the reasons we were just discussing, linear stops don’t get as much capacity as one might expect from the number of loading areas they have. An on-line linear stop with three loading areas only has two and a half loading areas worth of capacity.
Source:
R.K. Brail/P.J. Larrousse, Rutgers University
Image:
http://www.chicago-l.org/stations/images/Ohare/cumberland04.jpg

## Slide 45: Linear Loading Area Efficiency
Fourth and fifth loading areas add little additional capacity
Measures that decrease average dwell times may have a greater capacity benefit than adding loading areas
Source: TCRP, Transit Capacity and Quality of Service Manual. 2013.
Notes: This table illustrates the effective capacities of linear bus stops based on on-line or off-line design and other factors. Note that the on-line designs are less efficient than the off-line designs. We will use these values later in the course to calculate capacities.
Having three linear on-line loading areas provides 2.45 times the capacity of a single loading area. Adding another two loading areas (for a total of five) only increases the capacity effectively by ¼ of the capacity of a single loading area, but takes up much more space.
Source: National Transit Institute, “Transit Capacity and Quality of Service Course,” 2003.

## Slide 46: Bus Stop Size Constraints
Block lengths
On-street parking and other community needs
Passenger walking distance
Driveway locations
Ability of buses to maneuver around each other at stop
Notes: Aside from service requirements, bus stop design must also consider physical design limitations. Block lengths and driveway locations physically constrain a stop. Maintaining on-street parking for businesses/residences is another physical constraint. As the number of loading areas grows, passengers may become unsure where to wait for their bus at the stop and may have to walk a couple of bus lengths to get to the bus, increasing dwell times. The loading area design affects whether a bus can leave immediately when it’s ready to go, or whether it has to wait for a bus in front.
Source: National Transit Institute, “Transit Capacity and Quality of Service Course,” 2003.

## Slide 47: Basics of Demand Forecasting

## Slide 48: Why Forecast Demand?
Determines ridership and revenue for new projects and major service changes
Helps select appropriate level of service for a route
Creates basis for ordering needed equipment and facilities
Assists the long-range strategic planning process
Enhances political and community support for transit investment
Notes: Whether you are planning a new route or making modifications to an existing service, it is wise to forecast the demand. On one hand, this helps to determine whether ridership and revenue levels will be adequate. If so, the forecast will help in planning for equipment and facility needs. Demand forecasting is part of a service planner’s due diligence.
Source:
R.K. Brail/P.J. Larrousse, Rutgers University

## Slide 49: When to Use Demand Forecasting
Estimate overall demand for a new transit route
Estimate changes in demand based on changes in service levels or pricing
Notes: Demand forecasting is most important for new transit services, but it also may be worthwhile when evaluating a change to an existing service.
Source:
R.K. Brail/P.J. Larrousse, Rutgers University

## Slide 50: Forecasting Topics
Trial implementation
Comparisons
Elasticities
Network modeling
Discrete choice methods
Notes: The methods of demand forecasting can vary depending on a number of factors.
For minor service changes, it may be appropriate to experiment in the market by implementing the change and observing customer response.
Minor changes can often simply be compared with another service that is similar.
Another fairly simple option is to predict ridership changes based on elasticities that have been measured.
More sophisticated methods are generally reserved for major service changes, such as the addition of a new route. These may include network modeling or discrete choice methods. We will not discuss these techniques in detail for this course.
Source: “Transit Demand Analysis” from UW-Milwaukee.

## Slide 51: Trial Implementation
Forecasting is not always necessary
Example: change service levels to examine ridership changes
Difficulties:
  Can be expensive
  Experiments are often brief
  Never a completely controlled experiment
Notes: Trial implementation is an approach sometimes used as an alternative to trying to carefully forecast a service change. Trial implementation means that the transit agency makes a service change and monitors the results. It is an actual experiment in real time. If the results are positive the change will stay in place, and if the results are inadequate the change will be reversed.
This method is often used for small changes that are unlikely to have a major impact on ridership. Using this method for new services is riskier, but also possible.
Source:
R.K. Brail/P.J. Larrousse, Rutgers University

## Slide 52: Comparisons
Compare with a similar existing service
For a route modification: How did a similar change affect another route?
For a new route: Does another route serve a similar set of land uses?
Notes: Minor changes can often simply be compared with another service that is similar. Using this method for new services is riskier, but also possible.
Source: “Transit Demand Analysis” from UW-Milwaukee.

## Slide 53: Elasticities
Elasticity = % change in A per % change in B
Price elasticity of ridership = slope of this graph
Fare
Ridership
Notes: Elasticities are used to analyze changes in transit service. Essentially, an elasticity represents the change in one variable that corresponds to a unit change in another variable. It assumes a proportional tradeoff, which is not always the case but produces useful estimates.
Most commonly used is the price elasticity of ridership. This represents the percent change in ridership that occurs when you raise the fair by 1%. Typical values are around -0.3.
The positive or negative sign shows the direction of the trend. For example, the lines on the graph are negative.
The graph also demonstrates how elasticity varies depending on trip purpose. Emergency and commute trips are not very flexible, and fare changes won’t affect them much. They have small elasticities. However, trips made for social or recreational purposes are more flexible, and travelers are more likely change their behavior due to a fare change. These have higher elasticities. It’s important to realize that not everyone is affected by a fare change in the same way.
Sometimes people describe elasticities using the terms “elastic” or “inelastic. Inelastic means the elasticity is small, from 0 to 1. Elastic means the elasticity is large, greater than 1. (Negative signs are disregarded for these terms.)
Image source: http://people.hofstra.edu/geotrans/eng/ch7en/conc7en/transportelasticity.html

## Slide 54: Elasticity Examples
If you are cutting fares by 10% and you know the price elasticity of ridership is -0.5 then…
  Ridership will change by:
  elasticity x % change in fare
  -0.5 x -10%
  +5%
Notes: Guide the class through this example.
In addition, with this estimate of the new ridership level, we could calculate what the new level of fare revenue would be to complete the financial analysis.

## Slide 55: Variation in Fare Elasticity
High Fare Elasticity
(Ridership More Sensitive)
Small urban areas
Sparse transit service
Low cost of driving
Low transit mode choice
Off-peak
Weekends
Feeder service
Low Fare Elasticity
(Ridership Less Sensitive)
Large dense cities
Rapid transit
High cost of driving
High transit mode choice
Peak period
Notes: We mentioned earlier that elasticity varies depending on a number of characteristics. Here are some examples of factors that are known to make transit ridership more elastic or inelastic.
Sources:
“Transit Demand Analysis” from UWM.
Taylor and Fink, 2002.“The Factors Influencing Transit Ridership: A Review and Analysis of the Ridership Literature.”
TCRP Report 95.

## Slide 56: Selecting Appropriate Level of Service
Notes: Usually the appropriate level of service will be selected based on your projected demand.

## Slide 57: Bus Service Types
Determine the appropriate type of service (e.g., local, express, etc.)
Source: TCRP Report 111. Elements Needed to Create High Ridership Transit Systems. 2007.
Type of Service |  | Weekday Peak Period | Weekday Whole Day | Weekday Off-Peak and Weekend
Radial Line Haul Routes: | Boardings per VRH | 30 | 24 | 18
Urban Classes (buses >=30 ft.): | Boardings per VRH | 30 | 24 | 18
Suburban Classes (buses >=30 ft.): | Boardings per VRH | 15 | 12.5 | 10
Express Routes: | Boardings per trip | 23 | 23 | 23
All Classes (buses <30 ft.): | Boardings per VRH | 12 | 11 | 10
Notes: This table is used to select the appropriate type of service based on a known level of demand per VRH (Vehicle Revenue Hour).
Source: TCRP Report 111. “Elements Needed to Create High Ridership Transit Systems.”

## Slide 58: Service Headways
Transit agencies may have policies that dictate how the routes operate. For example:
  All routes will be operated on a clock headway system
    Round values of 60, 30, 20, 15, 12, 10, or 5 min
  Headways are determined by ridership demand
Notes: This slide introduces the application of Board Policy on service design issues.
These policies can be a mixed bag regarding maximization of operational efficiencies. They are balanced by marketing and public perception opportunities.

## Slide 59: Clock Headway Policy
Advantages
Easy for passengers to remember
Excellent marketing tool
Appeal to new riders inexperienced with the system
Disadvantages
Don’t always match perfectly with route timing
Don’t recognize peak hour traffic differentials
Can be a cost driver with additional layover and recovery time to make the service “fit the clock”
Notes: This slide details the balance between marketing opportunity, public perceptions and economies.

## Slide 60: Frequency and Capacity
Policy headways – desired frequency of service
Clock face headways benefit everyone
Passenger volume driven – bus capacity limits frequency of service headways during heavy use time
Vehicle capacity includes vehicle loading areas, bus lanes and seating
Notes: There is a sort of tension between focusing on capacity and focusing on frequency in service design. A convenient, frequent service may provide much more capacity than is needed -- but a service providing the minimum capacity for its demand may tend to be infrequent and unattractive for riders.

## Slide 61: Resource Allocation and Budgeting

## Slide 62: How Many Buses Needed?
Notes: This is the fundamental equation to find out how many buses a route needs. We will get into more detail about this in Module 6, but the basic principle is very straightforward. If a route takes an hour to cycle through, and you want to have a 30 minute headway, you’re going to need two busses running.
This calculation sets the starting point of the amount of work that we will need our drivers to do. Next, the bus trips get divided up into blocks.

## Slide 63: Key Principles of Blocking
A vehicle block is the set of trips that one particular bus does in the course of a day
Capacity of layover point for buses to meet needs to be considered
Assume bus operates out of the closest garage and/or where it enters revenue to reduce costs
Consider layover time requirements
Interlining can be done between routes to add efficiency
Notes: This slide introduces the key principles of blocking. It begin to add more process definition of the things that need to be considered when you are planning what a bus operates on during the period of the day.
It emphasizes the consideration of layover point and related amenities (that was introduced earlier in this section.)
It introduces a practical review of assigning buses out of the nearest garage in order to reduce deadhead costs.
It emphasizes layover time as it related to labor union agreements and required state laws.
And finally it introduces creative scheduling of having one bus operated on more than one route during the day in order to increase efficiency (interlining.)

## Slide 64: Key Principles of Runcutting
Runcutting is the task of creating driver work assignments from the schedule
By cutting and recombining vehicle blocks of time into daily driving assignments, a work schedule is created
Relief points are designated as part of the process in order to facilitate a shift change
Notes: After blocking is done to decide what vehicles will be operating which routes, then driver work assignment must be created.
These assignments are developed on a daily basis and then gathered into pieces of work for the bus operator bidding process.
Run cutting is made vastly more complicated if it has to conform with a large number of rules restricting the kind of duties that can be made. For example, many union contracts call for a minimum percentage of straight runs, limit the number of part time duties, and prevent split runs from starting before or ending after a certain time.
In order to properly plan for a shift change, consideration of where the relief points will be located as well as our the drivers will get back to the garage from the relief points should be considered.

## Slide 65: Run Cutting
Chart: Vehicles in Service
| AM peak | Mid-day | PM peak | Late night
Vehicles in Service | 97 | 78 | 113 | 34
Straight run
Straight run
Split run
Notes: CLICK ONCE to show the straight runs.
CLICK AGAIN to show the split runs.

## Slide 66: Work Rule Impacts
Most labor agreements include requirements and processes that must be followed when scheduling and bidding work. For example:
  Minimum amount of work that must be paid
  Whether or not you can have split shifts, and how many split shifts you can have
  How long can the work be split over the course of a 24 hour period
  How long a driver can operate a bus
  How the work can be assembled for the bus operators to bid on
  If there is a premium pay or penalty payments
Notes: All of these items have operational impacts as well as cost impacts.
The application of these work rules can reduce efficiency unless properly analyzed and applied through the schedule development and implementation phases.

## Slide 67: Cost Factors
Minimum guarantees
Overtime calculated based on labor agreement
Meal and rest breaks
Rostering
Requirements to limit split shift and maximize straight shifts
Extra board supply
Notes: Minimum guarantees-mandate that bus operators are guaranteed a minimum payment of X hours every time they work a shift
Overtime can be calculated on a daily basis or on a weekly basis depending on the agreement
Meal and Rest Breaks-California state law mandates that each bus operator be given a 30minute unpaid meal breaks and 2 –paid breaks for each 8 hour shift worked.
Rostering conditions are details regarding how the work assignments can or cannot be grouped when bus operator bidding occurs
Some agreements have a limit to how many split shift work assignments can be created and how long the span of service for the split shifts can be.