## Slide 1: Module 4
Transit Service Planning

## Slide 2: Goal
This module seeks to have students understand public transit service planning.
Notes: Full version:
This module seeks to prepare participants to practice public transit service planning. The benefits of transit, how transit can meet community goals, and key concepts of the legal and political environment will be introduced. Additionally, the course will provide an overview of available modes, operational concepts, and various system sizes. Participants will gain an understanding of network design theory, as well as service policy performance metrics. By the end of the course, participants will be able to undertake conceptual service planning/design and redesign, including routing and scheduling, transit budgeting, and calculating levels of service and capacity.

## Slide 3: Module 4, Lesson 1
Public Transit Planning in the US

## Slide 4: Learning Objectives
Discuss the history of public transit in the US
Summarize the variety of transit modes and their attributes from a planning perspective
Describe the typical duties of a transit service planner
Notes: Learning Objectives:
  Discuss the history of public transit in the US
  Summarize the variety of transit modes and their attributes
  List the benefits of transit for local communities
  Describe the demographic breakdown of transit riders
  Describe the typical duties of a transit service planner

## Slide 5: Historical Background

## Slide 6: Public Transit History: 1900 – 1940
As cities grew, private streetcar lines expanded
  Enabled cities to absorb thousands of new residents as the country became more urbanized
Trips decreased during the Depression
1917 Raleigh, NC
1920s Detroit, MI
Notes: Key Message: Growth of public transit, especially streetcars, enabled cities to absorb their population growth between 1900 and 1940.
Background Information: Street car lines were vital to growth of cities at the turn of the 20th century. As city populations exploded, residents were forced to live further and further from the city and its traditional workplace locations. Street cars allowed those living further out to fairly quickly access the city center and their jobs. Hence, “street car suburbs” emerged as one of the first forms of suburban sprawl, the key difference being that residents relied on mass transportation to leave home, therefore for the most part restricting residents to living within a half-mile radius or so of a station.
Transit use peaked in early 1920s, when Americans averaged 250 trips by transit per year.
With the depression, however, came less money and less travel. Additionally, by the end of the 1920s, buses were beginning to replace street cars.
Electric streetcars were the main source of public transportation in the first two decades of the 20th century. Streetcars were located mostly on city thoroughfares, and a few dedicated interurban ways. The 1,500 miles of track in 1890 had grown to more than 19,000 miles in 1920. By the mid-1920s, street car ridership had peaked and was starting to decline. More flexible buses and private vehicles drew away ridership. By 1951, there were less than 10,000 miles of track. Today, streetcars are making a comeback in cities such as New Orleans; Portland, OR; Tampa, FL; and Atlanta.
Sources: TCRP, “Making Transit Work”; USDOT, http://fastlane.dot.gov/2012/01/streetcar-forum.html
Sources: Britannica, “Mass Transit”
Image sources:
http://raleighphilosociety.blogspot.com/2008/07/state-archives-raleigh-photos-now.html
http://atdetroit.net/forum/messages/6790/61876.jpg

## Slide 7: Streetcar Suburb – Peabody Heights/Charles Village, MD
½ mile
3 miles to Downtown Baltimore
Notes: Key Message: 10 minutes is still a ½ mile walk to the streetcar, but the streetcar made it possible for people to live farther from downtown.
Background Information: Researchers have found that the time people spend traveling has remained relatively constant across time, place, and culture. The distance people are willing to travel increases as the speed at which they travel increases, but the time remains the same. Technological progress in the late 19th and 20th centuries has made it possible for us to travel faster, increasing the distance that can be covered in the same amount of time. This is evident with street cars suburbs, as people could still travel the same amount of time as they had done previously by foot and horse while covering more distance. This allowed cities to become larger and more dispersed; however, suburbs during this time were mainly built along streetcar lines, which meant they remained quite dense, such as Peabody Heights/Charles Village, MD.
Sources: Bloustein TLU PowerPoint

## Slide 8: Public Transit History: 1940 – 1960
World War II increased the demand for public transit
Streetcars were replaced with buses
Ridership ultimately declined as the suburbs and car ownership grew
Source: APTA, Transportation Fact Book: 2011, Appendix A: Historical Tables
Chart: Unlinked Passenger Trips by Mode, 1940 - 1959
| 1940 | 1941 | 1942 | 1943 | 1944 | 1945 | 1946 | 1947 | 1948 | 1949 | 1950 | 1951 | 1952 | 1953 | 1954 | 1955 | 1956 | 1957 | 1958 | 1959
Bus | 4255 | 4948 | 7264 | 9070 | 9713 | 9946 | 10247 | 10374 | 10759 | 10193 | 9447 | 9227 | 8901 | 8280 | 7643 | 7269 | 7062 | 6903 | 6540 | 6498
Commuter Rail | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Paratransit | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Heavy Rail | 2382 | 2421 | 2566 | 2656 | 2621 | 2698 | 2835 | 2756 | 2606 | 2346 | 2264 | 2189 | 2124 | 2040 | 1912 | 1870 | 1880 | 1843 | 1815 | 1828
Light Rail | 5951 | 6085 | 7290 | 9150 | 9516 | 9426 | 9027 | 8096 | 6506 | 4839 | 3904 | 3101 | 2477 | 2036 | 1489 | 1207 | 876 | 679 | 572 | 521
Trolleybus | 542 | 669 | 918 | 1220 | 1292 | 1298 | 1354 | 1398 | 1558 | 1691 | 1686 | 1658 | 1666 | 1587 | 1387 | 1223 | 1163 | 1003 | 843 | 749
Notes: Key Message: After WWII people moved out of cities and into the suburbs, where car ownership was necessary, and trips by car increased while transit trips rapidly began to fall.
Background information: The decline in transit ridership in the 1930s was reversed during World War Two. As the chart show, ridership of all modes increased after 1940, peaking in 1946, due to the rationing on gas and other elements of cars that made them more expensive. Ridership of trolleybuses and light rail in particular increased. After the War, however, cars became cheaper, as did housing far from city centers. Transit ceased being financially viable compared to automobile transportation.
Sources: TCRP, “Making Transit Work”; APTA, Transportation Fact Book: 2011, Appendix A: Historical Tables

## Slide 9: Early Auto City – Chevy Chase, MD
1 mile
6 miles to Downtown DC
Notes: Key Message: The advent of the automobile made it possible for people to live even farther out from the city center. However, before World War Two, suburbs were still located fairly close to city centers and car ownership had yet to reach the heights it would soon see, meaning that transit was still vital to many Americans.
Background Information: Chevy Chase, MD is an example of a community mostly developed between 1920-1940 (the city was originally 1 mile in radius). Such a size was a reasonable compromise size for a public that had cars but also did a lot of walking. At typical urban auto speeds in 1930, the trip to downtown was a 10-15 minute commute.
Sources: Bloustein TLU PowerPoint

## Slide 10: Auto-Freeway City – Columbia, MD
8 miles
35 miles to DC
Notes: Key Message: Freeways further increased the distance a person could live from the city center, and still get there in the same amount of time.
Background Information: Columbia, MD is an example of a typical car-dependent suburb. It is 8 miles wide, which means that a car must be used to drive across it. Depending on traffic, it would take the same amount of time to do so – about 10 minutes – as it would to walk the half-mile across Peabody Heights/Charles Village, the street car suburb. Columbia is also far from downtown Washington DC, enabled by cheap land and transportation. Sprawling, disconnected locations means that public transit struggles to compete with the efficiency of private vehicles.
Sources: Bloustein TLU PowerPoint

## Slide 11: Public Transit History: 1960 – 1980
Ridership declined, driven by suburban growth and stagnant or declining downtowns
Public sector had taken over most transit companies
An increase of federal funds prevented transit’s absolute decline
  1964: Urban Mass Transportation Act, provided $375 million in capital assistance over 3 years. The beginning of federal funding for mass transit
  1974: National Mass Transportation Assistance Act, authorized for the first time federal funds for transit operations
Notes: Key Message: A multitude of factors – including inner city troubles and the affordability of cars and suburban houses – caused transit ridership to decline rapidly during this period. However, the federal government stepped in and began to invest in transit.
Background Information: The exodus from cities and the rise of sprawling suburbs continued to cause transit ridership to decline.
As transit agencies stopped being profitable, some were taken over by the public sector to continue providing transportation as a public service. Others just shut down entirely.
Starting in 1964, the federal government stepped in to stop its absolute decline, with the 1964 Urban Mass Transportation Act. The Act provided $375 million capital assistance over three years.
Finally, in 1974, the National Mass Transportation Assistance Act for the first time authorized the use of federal funds for assistance with transit operation, broadening the use of federal funds and allowing state and local governments more flexibility. It required urban areas to coordinate multimodal transportation planning with a long-range planning requirement.
Sources: Weiner, Edward, “History of Urban Transportation Planning”; TCRP, “Making Transit Work”; FTA, History

## Slide 12: Public Transit History: 1980 – 2000
  1982: Surface Transportation Assistance Act, began the unification of highway, transit, and transportation safety programs
  1983: 5¢ gas tax increase, with 1¢ for transit
  1991: Intermodal Surface Transportation Efficiency Act (ISTEA)
    More flexibility with project selection
    Expanded number of transit programs
Notes: Key Message: A series of transportation bills, building on early ones from the 1960s and 1970s, helped stave off transit’s absolute decline.
Background Information: The federal government continued to expand public transportation funding during this era, including raising the gas tax, increasing the number of transit programs, and allowing greater flexibility in project selection. For example, the ISTEA legislation included the Congestion Mitigation and Air Quality (CMAQ) program to help regions comply with the new clean air standards, and required that states allocate a portion of their funds to MPOs.
Sources: Transportation For America, “Transportation 101: An Introduction to Federal Transportation Policy”; USDOT, “Legislation, Regulations, and Guidance: Intermodal Surface Transportation Efficiency Act of 1991 Information”; Weiner, Edward, “History of Urban Transportation Planning”

## Slide 13: Public Transportation Ridership Trends
Between 1995 and 2009:
  Ridership grew 34%
  Portion of work trips made using public transit increased from 3.26% to 3.32%
    Work trips are 59% of all transit trips
Source: National Household Travel Survey, 2009.
Notes: Today, transit ridership continues its steady growth as the nation becomes more urbanized. The most common trip purpose that transit serves is the commute trip – 60% of all transit trips are made to get to and from work. But viewed from the commuter perspective, transit still represents a small share of that market. Transit still has a long way to go to become a good option for more Americans.
Sources:
NHTS 2009 APTA, Transportation Fact Book: 2011
APTA, Profile of Public Transportation Passengers

## Slide 14: Transit Commuting Varies Geographically
Notes: New York City dominates the national data on public transit, as it has 40% of the nation’s unlinked transit trips.
Point out the other top metropolitan areas.
Also briefly discuss the unique challenges of transit in rural areas.

## Slide 15: Linked vs. Unlinked Trips
Important concept for measuring travel
Linked trip – entire journey from origin to destination
Unlinked trip – segment of a journey made using one vehicle
Notes: The distinction between linked and unlinked trips is important as we discuss statistics about transport.
Explain: Raw data from the transit farebox will be unlinked trips. If every traveler is making one transfer, then the number of linked trips is half as many.
Trip linking is NOT the same as trip chaining (e.g. stopping at an extra destination on the way from work.)
Also, note that NEITHER of these metrics represents the number of individuals using your service. A traditional transit commuter makes two linked trips on transit per day – and if transfers are involved then there will be even more unlinked trips. Determining the number of individuals your system serves requires a bit of calculation from the trip numbers.

## Slide 16: Typical Duties of a Service Planner

## Slide 17: A Day in the Life…
Service planners spend their days performing the following duties:
  Data review
  Field observations
  Community consultation
  Issue resolution

## Slide 18: Data Review
United States Census
American Community Survey
Other sources
Geographic data (GIS)
Running time data (AVL)
Passenger count data (APC) and advanced fareboxes
User/rider survey data
Data is so voluminous that care in selection of relevant data points should be taken.
Notes: The data is useless without a comprehensive understanding of what the data is measuring; the plans resulting from this lack of understanding can give rise to the often true observations of the public that the “people who plan these bus routes never ride the buses.”
Image:
http://www.flickr.com/photos/r-h/63359584/

## Slide 19: Field Observations
Riding the transit system to observe operational and community issues
Personal experience makes the data real
Allows for detection of errors
Although data says what is happening it does not tell us why – field work is necessary
Notes: The AVL system tells us that a particular bus trip is chronically late; is it late because it does not have enough running time, because the driver is driving especially slowly because they are socializing with a friend who always riders that particular trip, or for some other reason?
The scheduled times of two routes on two different southern California transit agencies suggested that at a particular location an excellent transfer opportunity existed. However, observations of the transfer location showed that one bus was chronically late, and arrived at the transfer location about one minute after the other bus left. As a result, the schedules were adjusted to insure the connection.
Image:
http://www.flickr.com/photos/michaelpatrick/1046671269/

## Slide 20: Community Consultation
Conducting public hearings, community charrettes, Advisory meetings, chamber committees and transportation board meetings
Requesting input from community at large, riders, drivers, supervisors and other transit employees
Understanding public perception is critical
Seeking solutions for problems identified
Notes: Under this definition, planning is a success if the public views it as successful. A limited stop bus route operated was only four minutes faster than the local bus route operating along the same corridor, which was approximately ten miles long. From a planning perspective, the limited stop route was a failure because of the negligible time savings. However, the public viewed it as much faster than the corresponding local route and therefore viewed the limited route as highly successful. As a result, the limited stop route was kept in operation.
Picture Source: http://thebrooklynink.com/2013/03/13/51904-a-new-bus-to-solve-their-problems-spring-creek-residents-not-so-sure/

## Slide 21: Issue Resolution
Developing new routes
Troubleshooting route problems
Responding to complaints
Analyzing service requests
Meeting to coordinate services
Communicating route performance status to community leaders; writing letters and Board reports
Notes: Major service changes, including the addition or subtraction of routes, changes in route frequency, and changes in the service span of a route are generally worked on by agency service planners.
Ridership data generated is extensively used by planners to ensure that agency resources are deployed in the most efficient way possible. In addition to ridership data, planners also use demographic and geographic data to identify opportunities for new routes.
Unfortunately, the economic climate of today has meant that most major service changes are service reductions; planners use service cut strategies in an attempt to minimize ridership losses accruing from the cuts.
Image:
http://www.flickr.com/photos/ooohoooh/1350774047/

## Slide 22: Modes of Transit
Notes: Several terms will be identified throughout this section. Remind participants to review the “Definitions List” located in the Appendix for clarification.
Note that the definitions used here are for conceptual service planning, and do NOT match the definitions used by the National Transit Database (NTD). (The NTD uses very precise technical definitions for the purpose of distributing formula funds.)
Source: Information for the following slides was developed from:
R.K. Brail/P.J. Larrousse, Rutgers University
NTI’s Building and Retaining Ridership course
NTI’s Transit Capacity and Quality of Service course
NTI’s BRT Workshop

## Slide 23: Mode Choice
Supply Characteristics
Type of technology
Capacity
Feasibility
Costs
Demand Analysis
Service area
Characteristics of demand – numbers, origins and destinations, client attributes
Based on supply characteristics and demand analysis
Notes: When considering the different modes of public transit, it is crucial to match the characteristics of the different modes (the supply) with the appropriate characteristics of your context (the demand).
In this section we discuss the supply side – issues such as the technologies the modes uses, their maximum capacities, constraints that will impact where they are feasible, and what level of investment is required.
The other side of the comparison is the demand analysis in your service area – this will be discussed later in the course, but it is important to keep in mind as we discuss the range of modes.

## Slide 24: Classifying Transit
Ownership/usage (private, for-hire, and public/ common carrier)
Characteristics:
  Right-of-way
  Technology
  Type of service
Notes: Transit modes can be classified in a variety of ways. In this course we aren’t going to focus on ownership, but it is worth noting that there are a variety of options to consider in the spectrum from public to private.
We will focus on describing transit based on the types of right-of-way. Does transit run in mixed traffic, or is it given some degree of separation to reduce delays?
The technology differences are also important to note. What is the means of propulsion? How is guidance provided? These factors can certainly affect the design of service.
And finally, types of service include different stopping patterns, times of operation, and distances of service.
Source: Vuchic
Image source: http://yptransportation.org/2012/03/26/nyc-job-alert-nyct-transportation-planner/

## Slide 25: Right-of-Way (ROW) – Categories
Category A – Grade separated, fully controlled
Category B – Runs at-grade with crossings, separated with curbs, barriers, or paint markings
Category C – Mixed traffic
Source: Vuchic, Vukan. Urban Public Transportation Systems. 1981.
Notes: Instructor: Organizer slide. These topics will be discussed on following slides. Mention and move on.
We will discuss right-of-way based on these three categories that range from a fully separated running way to service mixing in with auto traffic.

## Slide 26: Category A – Grade Separated
Rail and some BRT systems
Elevated or underground
Guided technology
Inherently reliable and fast
Strong connection between ROW class and speed/capacity costs
Very high level of investment
Source: Vuchic, Vukan. Urban Public Transportation Systems. 1981.
Chicago, IL
BRT Busway, Pittsburgh, PA
Notes: Category A is the optimal right-of-way for transit. This category separates transit from traffic completely. This can mean that transit is elevated or placed underground. Examples include heavy rail and some BRT systems. It is often a costly strategy, but it also has huge payoffs in terms of speed and capacity.
Image: http://www.flickr.com/photos/incendiarymind/2285886887/

## Slide 27: Category B – At-Grade
LRT and most BRT fit in this category
May include a combination:
  ROW A – fully controlled, grade-separated sections
  ROW C – mixed traffic sections
Considerable investment required for construction and maintenance
Source: Vuchic, Vukan. Urban Public Transportation Systems. 1981.
Seattle, WA
Notes: Partially separated rights-of-way have some separation from traffic but also do interact with autos at some points. One example might be a BRT line that has a separated ROW for most of the route, but mixes with traffic through a downtown district. Another example could be a light rail line that has to contend with auto traffic at certain intersections. Category B right-of-way provides may of the same benefits as Category A – increased speed and capacity – but with less infrastructure investment.
Image: http://www.flickr.com/photos/camknows/4560293253/

## Slide 28: Category C – Mixed Traffic
Buses, paratransit, trolleybuses, trolleys
Slow and least competitive with auto
Tends to serve riders who don’t have other travel choices
Most bus service is in this category
Minimal investment
Source: Vuchic, Vukan. Urban Public Transportation Systems. 1981.
Seattle, WA
Notes: Finally, Category C right-of-way means service that mixes on-street with auto traffic. It can be very slow and unpredictable where traffic is congested, and so it isn’t likely to attract people who have other travel options. However, because it requires minimal investment in infrastructure, it has become the most prevalent form of transit ROW.
Image: http://www.flickr.com/photos/viriyincy/3618661218/

## Slide 29: Types of Service
Route and trip type
Stopping schedule
Time of operation
Notes: Next, we will discuss the types of service based on distances of service, different stopping patterns, and times of operation.
Image source: http://abclocal.go.com/wls/story?section=news/local&id=7338292

## Slide 30: Route and Trip Type
Short-haul – low-speed, small areas, high travel density, many stops (e.g., airports, central business districts)
City-wide – routes serving entire city
Regional – high-speed, longer trips, fewer stops (e.g., Regional rail, express bus)
Notes: Short-haul routes are short routes that often serve a specialized purpose, like a neighborhood or downtown circulator.
City-wide routes are much longer, connecting people traveling between different districts of a city.
Regional routes are even longer, and have fewer stops, connecting different communities in a region.

## Slide 31: Stopping Schedule
Local service – all stops
Accelerated service – skip-stop
Express service – widely spaced stops
Notes: A similar way to consider service is the stopping pattern:
Local services have closely spaced stops to provide an area with easy access to transit, though often at the cost of a lower speed.
Accelerated services may use strategies like skipping stops to speed up service a bit, while maintaining a significant portion of the local stops.
Express services prioritize speed over stop access – by only serving the most popular stops, express routes can cut travel times dramatically.
Source: http://web.mta.info/mta/planning/sbs/whatis.htm

## Slide 32: Time of Operation
All-day
Peak-periods
Irregular – special events
Service levels vary between
  Weekdays, Saturdays, Sundays
  Weeks and months in a year (e.g., campus transportation systems)
Notes: Services can also vary in the hours they are operated.
  All-day
  Peak-periods
  Irregular – special events
  Service levels vary between weekdays, Saturdays, Sundays
  Weeks and months in a year (e.g., campus transportation systems)
  Source:
  http://www.transitchicago.com/schedules/, http://www.baymetro.com/routes-schedules

## Slide 33: Bus Transit Modes

## Slide 34: Bus – Overview
Largest ridership of any form of transit
Flexible
  Route locations
  Vehicle types and sizes
  Right-of-way types
  Service types
Wide variations in speed and capacity
Low capital costs
Notes: Bus transit has the largest ridership of any mode of transit – 5.5 billion trips out of 10.4 billion trips (53%) in 2009.
One of the bus’ main benefits is its flexibility. It can be routed anywhere the street network will allow. It can use low-capacity minibuses or high-capacity articulated buses. Buses can mix in with auto traffic or have a separated right-of-way. And service can use a variety of approaches depending on the context.
Buses are typically conceptualized as running in low-capacity low-speed local service, but with the popularity of BRT bus services, we know high-capacity high-speed bus service certainly is possible.
And most importantly, bus service is inexpensive from a capital perspective. Running on existing roadways is a lot less costly than constructing rail tracks or a new right-of-way.

## Slide 35: Bus – Vehicle Types
Vehicle design affects:
  Capacity
    Passenger capacity (seated/standing)
    Internal circulation
    Number of doors/channels
    Floor height
  Quality of service
    Number of seats
    Ride comfort
    Ability to access particular areas
Community issues
  Vehicle size, noise and exhaust
Notes: There are various types of bus vehicles to chose from. From the transit agency perspective, a key consideration is capacity and the comfort that will be provided to your passengers. The community may also have an interest in the vehicles due to concerns over noise and exhaust.
Internal circulation affects how easily passengers can clear the door area, allowing others to board.
Wider doors allow two passengers to pass through the door at once; more doors allow more passengers to board and/or alight at once; both affect dwell time.
Low-floor buses (without steps) are quicker to board.
The selection of a particular vehicle to use may also hinge on quality of service concerns and community “quality of life” issues.

## Slide 36: Bus – Vehicle Types
Vehicle design affects:
Community issues
  Vehicle size, noise and exhaust
    Capacity
    Passenger capacity (seated/standing)
    Internal circulation
    Number of doors/channels
    Floor height
    Quality of Service
    Number of seats
    Ride comfort
    Ability to access particular areas
Notes: There are various types of bus vehicles to chose from. From the transit agency perspective, a key consideration is capacity and the comfort that will be provided to your passengers. The community may also have an interest in the vehicles due to concerns over noise and exhaust.
Internal circulation affects how easily passengers can clear the door area, allowing others to board.
Wider doors allow two passengers to pass through the door at once; more doors allow more passengers to board and/or alight at once; both affect dwell time.
Low-floor buses (without steps) are quicker to board.
The selection of a particular vehicle to use may also hinge on quality of service concerns and community “quality of life” issues.

## Slide 37: Bus – Service
Fixed route
  Provided along a designated route and operated at set times or headways
  Three types – local, limited-stop, and express service
  Bus Rapid Transit (BRT) combines express service with improved infrastructure
Paratransit or Demand Responsive Transit (DRT)
  Variable route, activated in response to users’ requests
  Provided as shared ride (typically door-to-door or curb-to-curb) and on a point-to-point basis

## Slide 38: Bus – Facilities
Least Exclusive
Most Exclusive
Arterial
Bus Lanes
Freeway HOV Lanes
Busways/
Transitways
Mixed Traffic
Notes: Outline Slide. Topics will be covered in following slides. Mention and move on.
Progressing down the list, you get more separation (and less interference) from other traffic—capacity and travel speeds improve.
We will start at the top with Mixed Traffic.

## Slide 39: Mixed Traffic Operation
Most common bus operating environment
Accounts for over 99 percent of total bus route distance in North America
Easily done, cheap, expected
Interrupted flow
Buses share their lane with general traffic
Potential for delays from a variety of sources
Mixed Traffic
Notes: Mixed traffic bus statistics:
Capacity = 7,380 pass/hr
Avg. speed = 12.6 mph
Avg. trip length = 3.9 mi
Operating cost per vehicle revenue hr = $120
Source: Canadian Transit Handbook, APTA Fact Book 2010

## Slide 40: Mixed Traffic – Bus Lane Types
Type 1
  One traffic lane in direction bus operates
Type 2
  Two or more traffic lanes in the direction bus operates
Notes: Mention that these classifications will play a role later in the course when we seek to determine capacity.
There is not a Type 3 lane – Type 2 covers all multi-lane streets.

## Slide 41: Arterial Bus Lanes
One or more lanes reserved exclusively for buses
  Full-time or part-time
  Right turn, taxi exceptions
Flow interrupted by intersections
Other lanes may be shared with general traffic
Arterial
Bus Lanes
Notes: “Interrupted” means traffic signals, stop signs, etc. are present. Some arterial bus lanes allow general traffic in make right turns; others allow use by taxis.

## Slide 42: Arterial Bus – Lane Types
Type 1
  Buses must remain in a single lane
Type 2
  Buses may use adjacent lane, if traffic permits
Type 3
  Two lanes reserved for buses
  Single lane, with off-line bus stops
Notes: Mention that these classifications will play a role later in the course when we seek to determine capacity.
Type 1
  Contraflow lane (physically separated) with no passing opportunity (Lymmo downtown circulator).
  Could also use a contraflow lane not physically separated from other lanes
Type 2 – One lane reserved exclusively for buses, with bus use of left lane allowed.
  Example is from Montreal, Québec.
Type 3 – Dual bus lanes. Madison Avenue, NYC, used by 180 peak hour buses, carrying 10,000 passengers. Other examples include:
Portland bus mall, used by 175 buses, with 8500 boardings (some riders board and get off along the mall, which is part of a fareless zone, so loads are somewhat lower than would be indicated by dividing 175 buses into 8500).
South Dade Busway. Although it only has one lane, it provides passing areas at stops, which makes it a Type 3 lane. Although called a “busway”, it has traffic signals, which means it should be analyzed as an arterial bus lane for capacity purposes.
Right turns are prohibited from Type 3 bus lanes, but may be allowed in the other types of bus lanes.

## Slide 43: Freeway HOV Lanes
May be shared with 2+ or 3+ carpools
Intended to provide faster operations for HOVs
Uninterrupted flow
Can be concurrent flow or contraflow
Lanes may or may not be separated from other traffic
Off-line bus stops, if any
Range in length from miles to short congestion bypasses
Freeway HOV Lanes
Notes: If buses stop along the HOV lane, it must be out of the flow of traffic. This requires special left-side exits and entrances (adds capital costs), or right-side HOV lanes (which have traffic weaving issues).
Example is from Seattle.
Concurrent flow – lane in the same direction as general traffic
Contraflow – using an underutilized lane in the opposite direction
Freeway HOV Lane Capacity:
  Bus capacity generally will be constrained before or after HOV lanes. Central Business District bus distribution needs to be addressed
Other than the Lincoln Tunnel, bus volumes do not approach a freeway lane’s capacity
Highway Capacity Manual procedures can be used to calculate the vehicle capacity of an HOV lane shared with carpools

## Slide 44: Busways or Transitways
Busways/
Transitways
Facility typically used as a component of Bus Rapid Transit (BRT)
OC Transpo, Ottawa
Notes: **Note: For more information about Bus Rapid Transit, register for NTI’s BRT Workshop.

## Slide 45: Bus Rapid Transit
High-speed, high-capacity service
  Exclusive bus facility (busway or transitway)
  Vehicle flow with very few interruptions
  Measures to expedite passenger loading
  Specialized high-capacity buses
An excellent passenger experience
  Stations included rather than merely stops
  Use of unique signing, vehicles, or color schemes to distinguish BRT service
Notes: BRT – “An integrated system of facilities, equipment, services, and amenities that improves the speed, reliability, and identity of bus transit.” This list represents its main features.
Many services use what might be described as “BRT Lite” – they may lack the dedicated right-of-ways and often use fewer of the BRT elements.
Source: TCRP Report 118 “Bus Rapid Transit Practitioner’s Guide”

## Slide 46: BRT – Facilities
Busway – exclusive bus facility, grade-separated from traffic
Transitway – exclusive bus facility, at-grade with traffic
  Distinction affects how the facility is analyzed
Seattle, WA
Eugene, OR
Notes: Some BRT busways include elevated or underground alignments. For at-grade transitways, the lane may be located curbside or in a median.
Some facilities that may be called “busways” because they are used exclusively by buses (e.g., Miami’s South Dade Busway) are treated as arterial bus lanes for analysis purposes because they have traffic signals.
  Exclusive-lane BRT includes not only facilities in streets or freeways but also the use of offstreet right of way (most commonly abandoned rail lines).
Another term sometimes used is “Quickway” – this means a busway that includes a passing lane to enable local and express services to run concurrently.
Images are from:
  Seattle, WA, bus tunnel
  Eugene, OR, Lane Transit EmX
Image Sources:
http://citytransport.info/NotMine/U1997_0991a.jpg
BRT course

## Slide 47: BRT – Vehicle Flow
“Rapid transit” station spacing (stations spaced far apart for limited-stop service)
No traffic signals or stop signs
  Signal priority or pre-emption
  Automatic Vehicle Location (AVL) facilitates
  Queue jumping can also cut intersection delay
Bus stops are off-line, or include a passing lane
Notes: Main features:
High-speed, high-capacity service
  Exclusive bus facility (busway or transitway)
  Vehicle flow with very few interruptions
  Measures to expedite passenger loading
  Specialized high-capacity buses
  An excellent passenger experience
  Stations included rather than merely stops
  Use of unique signing, vehicles, or color schemes to distinguish BRT service
“Uninterrupted flow” means no traffic signals, stop signs, etc. that would cause traffic to stop.
Express and local service are both possible with BRT. In addition, an operation could enter and leave the BRT alignment.
Busway stations should provide opportunities for buses to pass each other (e.g., express vs. local service).

## Slide 48: BRT – Expedite Passenger Loading
In-station/off-board fare collection to expedite boarding
Low-floor boarding
Healthline – Cleveland, OH
Swift – Snohomish County, WA
Notes: Image:
http://www.flickr.com/photos/viriyincy/4129217919/
Cleveland Healthline

## Slide 49: BRT – Vehicles
40-foot and articulated 60-foot vehicles are common
  Most systems using or considering low-floor buses
May have doors on both sides to allow use of center-platform stations
Guided bus technology (curb-guidance)
  Permits narrower lanes or higher speeds for a given lane width
Most use conventionally-powered buses (internal combustion engines) but some are electric
Orange Line – Los Angeles, CA
Notes: Curb guidance may allow a small enough gap between bus doorways and station platform edges to accommodate wheelchair access without requiring a bridge plate – this reduces dwell time.
Image:
http://www.flickr.com/photos/fredcamino/2308756843/

## Slide 50: BRT – Passenger Experience
Stations included rather than merely stops
  Real-time information often provided
Use of unique signing, vehicles, or color schemes to distinguish service
Max – Las Vegas, NV
Green Line – Eugene, OR

## Slide 51: Paratransit
Paratransit is the most flexible mode:
  Activated in response to user requests (typically door-to-door or curb-to-curb)
  Variable route
  Provided as shared ride
Most common type of transit system because mandated by ADA
Most costly mode per-trip
Stockton, CA
Notes: Paratransit is the most flexible mode of public transit.
Another term for paratransit is Demand Responsive Transit or Demand Responsive Service. It includes a wide range of transit services defined as services that are not conventionally scheduled, fixed-route transit services, but rather those types of public transportation that fall in-between the private automobile and conventional fixed-route transit.
Paratransit is not exclusive to ADA, but the majority of paratransit exists because of a legal requirement for “complementary ADA service”. Paratransit services are the most prevalent systems of transit in the US because they are mandated under the Americans with Disabilities Act.
Paratransit Statistics:
Capacity = Very low
Avg. speed = 14.6 mph
Avg. trip length = 7.4 mi
Operating cost per vehicle revenue hr = $64
Source: Canadian Transit Handbook, APTA Fact Book 2010
Image: http://www.flickr.com/photos/san-joaquin-rtd/4518434320/

## Slide 52: ADA Complementary Paratransit Service
Public entities operating a fixed-route system shall provide complementary paratransit services for riders who cannot independently use fixed route service, due to disability
Does not apply to commuter bus, commuter rail, or intercity rail systems
Determined based on an individual’s ability to use fixed route system
NTI courses Comprehensive ADA Paratransit Eligibility and Paratransit Management & Operations
Notes: This requirement originates from the Americans with Disabilities Act, § 37.121.
Complementary paratransit is meant to be just that - a complement to accessible fixed-route service. It is not intended to be a separate service for all individuals with disabilities, but rather a safety net for those individuals who are not capable of independently boarding, riding, or disembarking from an accessible fixed-route vehicle or for a transit agency that is unable to provide an accessible vehicle or stop along a route. (§ 37.123)
Title II of the ADA prescribes that each public entity operating a fixed-route system shall provide paratransit (or other special service) to individuals with disabilities that is comparable to the level of service provided to individuals without disabilities.
Requirements for complementary paratransit do not apply to commuter bus, commuter rail, or intercity rail systems. ADA guidelines and requirements for accessibility standards still apply to these systems, even though they are not required to provide complementary paratransit service.
The following individuals are ADA paratransit eligible:
  Any individual with a disability who is unable, as the result of a physical or mental impairment (including a vision impairment), and without the assistance of another individual (except the operator of a wheelchair lift or other boarding assistance device), to board, ride, or disembark from any vehicle on the system that is readily accessible to and usable by individuals without disabilities
  Any individual with a disability who needs the assistance of a wheelchair lift or other boarding assistance device and is able, with such assistance, to board, ride and disembark from any vehicle that is readily accessible to and usable by individuals with disabilities
  Any individual with a disability who has a specific impairment-related condition that prevents such individual from traveling to a boarding location or from a disembarking location on such system.
**Note: Inability to get to and from the fixed-route in order to get to origins and destinations served by the fixed-route (e.g., by navigating the local sidewalks to get to the bus or rail stop) is a basis for eligibility under 49 CFR 123(e)(3).
**Note: Details concerning the requirements and regulations of Paratransit Eligibility are discussed at length in the National Transit Institute course, Comprehensive ADA Paratransit Eligibility.
Source:
49 CFR § 37.121
TCRP Legal Research Digest 19
NTI’s Understanding ADA course

## Slide 53: Paratransit Service
Private Car
Taxi
Demand Response Dial-A-Ride
Carpool and Vanpool
Jitneys
Subscription Bus/Van
Fixed Route
Paratransit Services
ADA Services
Notes: Paratransit Services that are also ADA:
        Taxi – Shared ride taxis are generally zone taxis. Exclusive ride taxis are generally meter taxis.
      Demand response/Dial-a-ride – Demand response service is where the passenger can call for an “immediate” real time ride. In ADA service, the passenger generally calls the day before to schedule a trip for the next day. The ADA demand response can also be pre-scheduled up to 14 days prior. Same day ADA service is possible, but not required under the ADA regulations.
      Subscription/Bus/Van – This can also be called “Standing Order” and refers to repeat trips, such as employment, dialysis, etc. FYI, FTA says you can have more than 50% subscription if you have no denials.
      Jitney – Fixed route with no fixed schedule; independently owned and operated.
Paratransit Services that are NOT ADA:
    Private car – The private car can be used in paratransit services, volunteer programs, carpooling, or voucher reimbursement programs.
    Fixed route – The fixed-route portion is a pre-scheduled trip that operates on a repeat basis to the point that fixed-route can be created. Generally, smaller vehicles, vans, or BOC vehicles are the vehicles of choice.
    The ADA services are required to serve customers who are unable to use fixed-route service. Service is required to operate on the same days and hours, within ¾ miles of any fixed-route bus lines, rail stations, and core service areas. The paratransit fare can be no more than double the fixed-route fare.
    Source: NTI course “Paratransit Management and Operations”

## Slide 54: Modes of Operation
One to One
Many to One
One to Many
Zone 1
Zone 2
Zone 4
Zone 3
Zonal
Fixed-Route Deviation
Many to Many
Notes: Paratransit consists of 6 modes of operation.
  One-to-one – A point-to-point service where you pick up one person and take them to their destination (e.g., exclusive ride taxi).
  Many-to-many – Many customers are picked up and there may be many shared ride trips being made (i.e., typical real time Demand Response service).
  Many-to-one – Pick up many customers and take them to one location (e.g., senior day care, a sheltered workshop). The reverse is One-to-many.
  One-to-many – Pick up many customers at one location and take them to many destinations.
  Fixed-route deviation – A fixed route can deviate from its regular route and make a demand or scheduled off-route pick up or drop off. Does not go beyond ¾ miles from the route and does not expand ¾ miles out, unless you change the fixed route.
  Zonal – The vehicle generally stays in one zone and provide trips within that zone (e.g., a train shuttle, employment center).
  Encourage participants to take the NTI course “Paratransit Management and Operations” to learn more about paratransit.
    Source: NTI course “Paratransit Management and Operations”

## Slide 55: Rail Transit Modes

## Slide 56: Rail Systems
Three major modes:
Light rail transit (LRT)
Heavy rail
Commuter rail
Memphis, TN
San Francisco, CA
Salt Lake City, UT
Notes: Rail transit systems in North America carry more than 5 billion passengers each year.
Light Rail: Memphis RTA (Wikipedia)
Heavy Rail: BART (Wikipedia)
Commuter Rail: FrontRunner (Wikipedia)

## Slide 57: Light Rail
Also called streetcar, tram, trolley
Can operate in a variety of rights-of-way
  Shared right-of-way mostly called “streetcar”
  Separated right-of-way mostly called “light rail”
Typically powered electrically, from overhead wires
  Third rail or diesel power are also options
Sacramento, CA
Notes: Light rail track-work and structures (but not cars) are generally lighter and less costly than rapid transit and commuter rail facilities, thus the name.
Features
  Quieter acceleration
  No diesel exhaust (typically)
  Require overhead wires unless dual-powered
Capacity = 6,060 to 22,700 pass/hr (varies depending on the use of exclusive lanes and the type of vehicle)
Avg. speed = 14.7 mph
Avg. trip length = 4.6 mi
Avg. station spacing = 0.52 mi
Operating cost per vehicle revenue hr = $245
Light rail – with relatively frequent service along mostly exclusive or segregated rights-of-way, using articulated cars and up to four-car trains
Streetcars – operate along mostly shared or segregated rights-of-way, with one-car (or rarely, two-car) trains, vehicle types and ages can vary
Vintage trolleys – provide mainly tourist or shopper-oriented service, often at relatively low frequencies, either historic vehicles or newer vehicles designed to look like historic vehicles
Sources: Canadian Transit Handbook, APTA Fact Book 2010
http://www.flickr.com/photos/paulkimo/401159937/

## Slide 58: Light Rail
Light rail stops at stations, not curbside
One or two-car trains typical (up to four)
Relatively short station spacing (0.5 mi typical outside downtown areas)
Most LRT systems have signal priority (sometimes pre-emption), generally using AVL
Charlotte, NC
Notes: AVL used for management of operations, and to provide information to passengers either or both in stations and on board buses.
Image (Patriarca12 at en.wikipedia) LYNX, Charlotte, NC

## Slide 59: Heavy Rail
Also known as metro, subway, underground, elevated rail, rapid rail, rapid transit
Chicago, IL
Los Angeles, CA
Notes: Image sources:
http://railfanning.org/graphics/chicago_3851.jpg
http://www.blogcdn.com/www.autoblog.com/media/2011/03/la-subway-630opt.jpg

## Slide 60: Heavy Rail
Fully grade-separated rights-of-way (separated pedestrian and vehicular crossings)
High speed and frequent service
Medium station spacing (typically 1-2 miles outside downtown areas)
Multiple-unit trains (up to 10-11 cars)
Third-rail power source (also catenary)
High level platforms
Notes: Statistics:
Capacity = 18,200 to 43,200 pass/hr (varies based on the design of the cars)
Avg. speed = 20.0 mph
Avg. trip length = 4.8 mi
Avg. station spacing = 0.91 mi
Operating cost per vehicle revenue hr = $199
Sources: Canadian Transit Handbook, APTA Fact Book 2010

## Slide 61: Commuter Rail
Generally a long-distance transit mode
Medium-to-long station spacing (often 2-5 miles or more outside downtown areas)
All passengers typically have a seat
Service is heavily oriented towards the peak commuting hours
Regional rail – a commuter rail system that provides high levels of all day service
Massapequa Park, NY
Notes: Also called metropolitan rail, regional rail, or suburban rail.
Services typically operated:
  Between a central city and adjacent suburbs
  Within urbanized areas, or between urbanized areas and outlying areas
  Generally characterized by multi-trip tickets, specific station to station fares
  Intercity rail service is usually excluded
Image source:
http://www.flickr.com/photos/thomconlon/945107882/

## Slide 62: Commuter Rail
May use track that is a part of the general railroad system and shared with freight – or track may be used exclusively for passengers
Self-propelled cars or locomotive-hauled
Baltimore-Washington Metropolitan Area
Notes: Statistics:
Capacity = 8,000 pass/hr
Avg. speed = 31.4 mph
Avg. trip length = 23.4 mi
Avg. station spacing = 3.55 mi
Operating cost per vehicle revenue hr = $480
Sources: Canadian Transit Handbook, APTA Fact Book 2010

## Slide 63: Other Transit Modes

## Slide 64: Other Modes
Ferry
  Auto, passenger
Monorail
  Straddle, suspended
Cable car
  Unique to San Francisco
Notes: Ferry
  Auto, passenger
  Provides a water connection between or among points where land routes are interrupted by water.
  Considerations include passenger and vehicle demand, dock configurations, speed, and environmental issues.
  Service types include: Point-to-point, Linear multiple-stop services, circulators, and water taxis.
  Intermodal transfers are usually required at one, and often, both ends of the ferry trip.
  Only monohulls and catamarans are used for ferry service in North America at this time.
Monorail
  Monorail vehicles straddle or are suspended from a single rail.
  Driverless monorails fall into the category of AGT.
Cable car
  Unique to San Francisco

## Slide 65: Other Modes
Automated Guideway Transit (AGT)
  Driverless vehicles for institutional circulation
Aerial ropeways
  Carrier suspended from aerial cable
Funiculars or Inclines
  Suited for hilly areas
Notes: Automated Guideway Transit (AGT): (Image from Miami)
  Driverless vehicles
  Short station spacing
  Downtown and institutional circulation
    Downtown people movers
    Airport terminal shuttles
    Amusement park circulation
    University, shopping mall, casino circulation
Aerial Ropeways: (Image from New York)
  Carry people or freight in a carrier suspended from an aerial rope (wire cable)
  The carrier consists of the following components:
    A wheeled carriage that runs along the rope and contains a fixed or detachable grip that clamps onto the rope
    Passengers ride in an enclosed cabin, a partially or fully enclosed gondola, or an open or partially enclosed chair
    These two pieces are connected by a hanger
Funiculars or Inclines: (Image from Pittsburgh)
  Funicular railways, also known as inclined planes or simply inclines, are among the oldest successful forms of mechanized urban transport in the United States
  Funiculars are well suited for hilly areas, where most other transportation modes would be unable to operate, or at best would require circuitous routings

## Slide 66: Summary of Modes by Capacity
Source: TCRP, Transit Capacity and Quality of Service Manual. 2013.
Notes: Passenger traffic density measures how many passengers are carried on average over a given mile of a route. It is measured as passenger miles per directional route mile.
Typical capacity ranges reflect ranges of train lengths and dwell times for rail; ranges of dwell times for bus.
Source: Transit Capacity & Quality of Service Manual