## Slide 1: Module 4, Lesson 2
Fundamentals of Transit Service and Networks

## Slide 2: Learning Objectives
Explain the key factors that drive transit demand
Summarize the main approaches to network design
Describe the role of intermodal coordination in transit planning

## Slide 3: What Drives Transit Demand?

## Slide 4: Three Perspectives on Demand
Transit Demand
Socio-economic factors of the community
Spatial factors of the service area
Transit agency factors
Notes: These three perspectives are commonly used in considering demand for transit.
Note that “forces traditionally outside the control of transit planners, managers and even policy makers may have greater impacts on ridership than any combination of traditional fare, marketing, service design, or operational initiatives.”
– TCRP Research Results Digest 4

## Slide 5: Socio-Economic Factors
Groups with limited access to private vehicles
  Children
  Elderly
  Disabled
  Low-income
  Low car ownership
High employment levels, especially in central location
Notes: Transit must compete with the automobile that dominates transportation in this country. Any demographic patterns that make driving less attractive will make transit more attractive.
Source: Taylor and Fink, 2002. “The Factors Influencing Transit Ridership: A Review and Analysis of the Ridership Literature.”

## Slide 6: Spatial Factors
Land uses generating travel
  Housing density
  Employment density
Difficult access via auto
  Low supply of parking at destination
  High price of parking at destination
  High tolls, congestion, gas prices also influence
Notes: The demand for transit can exhibit considerable spatial variation. As we mentioned on the previous slide, factors that make driving difficult make transit more attractive – so traffic congestion and a lack of free parking can go a long way towards generating transit demand. Also, there will be more transit demand where there is more travel overall – such as areas with dense housing or clustered employment.
Sources:
Taylor and Fink, 2002. “The Factors Influencing Transit Ridership: A Review and Analysis of the Ridership Literature.”
TCRP Report 111, “Elements Needed to Create High Ridership Transit Systems.”

## Slide 7: Transit Agency Factors
Fares
Quantity of service
Quality factors:
  Bus information
  Station safety
  Customer service
  Safety en-route
  Cleanliness
Notes: The actions taken by a transit agency do have an impact on ridership as well.
As you would expect, lower fares encourage more people to ride transit.
In general terms, the more investment there is in transit, the higher the level of transit patronage. Increases in the quantity of service can attract new riders, and it generally has a greater impact on ridership than decreasing fares.
It has also been shown (by Robert Cervero) that service quality factors can impact ridership at a similar level to the fare or the service quantity. The top five quality factors he identified are listed.
Transit must compete with other travel modes in all aspects of service, from access to reliability to travel time.
Sources:
Taylor and Fink, 2002. “The Factors Influencing Transit Ridership: A Review and Analysis of the Ridership Literature.”
TCRP Report 111, “Elements Needed to Create High Ridership Transit Systems.”

## Slide 8: Identifying Transit-Supportive Areas
Visualize the geographic patterns in transit demand
The Transit Capacity and Quality of Service Manual (TCQSM) identifies different levels of transit service that can be supported by different residential and job densities:
Notes: Applying this understanding of what drives transit demand, transit agencies can visualize how this demand is distributed geographically throughout their region. Understanding the geographic pattern of where demand is strong and where it is weak is crucial for service planners to make informed decisions regarding where service should be provided.
A minimum density of 4.5 units per net acre is a typical minimum residential density for hourly daytime transit service to be feasible. An employment density of approximately 4 jobs per gross acre produces the same level of ridership. These minimum density values define transit-supportive areas: areas which are capable of supporting at least hourly fixed route transit service.
Once you know where your transit-supportive areas are, you can also calculate what percentage of those areas is served by your transit network -- within a given distance of a bus stop or rail station.
Based on the previous slides, we know there is much more to transit demand than just the housing and job densities, so perhaps this method is a bit too simplistic. Still, it is a useful way to approach the question of where transit demand might exist.

## Slide 9: Example – Transit-Supportive Areas
Weighted sum of:
  Population per acre
  Jobs per acre
  Zero car households per acre
Classified into five categories
DVRPC, PA/NJ
Notes: Next we have some other examples of other approaches that have been used in determining the suitability for transit. This analysis of the Philadelphia and New Jersey region used a somewhat different set of criteria, as shown on the slide.
Different areas may use different metrics for determining suitability for transit.
Source: www.dvrpc.org/reports/07005.pdf

## Slide 10: Example – Transit-Supportive Areas
La Crosse, WI
Fixed-Route Transit Propensity |  |  |  |  | 
Variable | Very Low | Low | Moderate | High | Very High
0 vehicles | All of the variables fell below the lower limit | 2 of 3 of the variables fell below the lower limit | 5.0%-10.4% | 2 of 3 of the variables exceeded the upper limit | All of the variables exceeded the upper limit
Minority |  |  | 4.4%-7.8% |  | 
Poverty |  |  | 7.2%-13.7% |  | 
Notes: Here is a similar example from La Crosse, WI, using yet another set of criteria. The creators of the map also highlighted the high-demand areas that were lacking in service – these areas might be prioritized for future service.
The table appears after one click. It illustrates the specific criteria used to assess which areas are transit-supportive: Zero vehicle households, minority population levels, and poverty levels.
(The route buffers shown here as the “service area” are ¼ mile.)
Source: Taylor and Fink, 2002. “The Factors Influencing Transit Ridership: A Review and Analysis of the Ridership Literature.”
Graphic: http://www4.uwm.edu/cuts/utp/demand.pdf

## Slide 11: Network Design
Notes: We will talk about both the street network and the transit service network.

## Slide 12: How Large is the Catchment Area?
Common rules of thumb: Travelers will walk ¼ mi or ½ mi to transit
FTA funds pedestrian improvements within ½ mi of transit
FTA funds bicycle improvements within 3 mi of transit
Notes: A fundamental question to consider in designing a transit network is how far you expect your customers to walk to reach the service? How large is the catchment area – that area from which passengers will be drawn around a transit stop or station?
The common rules of thumb are that people will walk ¼ mile to a bus service or ½ mile to a rail service.
Ask: What standards are used by the agencies represented in the class?
Transit trips are often “multi-modal” journeys, and all modes should be considered in evaluating effective access to the main transit mode or facility. The quality of surrounding infrastructure is key to ensuring your transit service truly is accessible. More on intermodal connections will be covered later in this module.
FTA funding criteria are for Joint Development projects near stations or stops.
Sources:
Blueprint Denver (image)
Transit JD, USDOT Railvolution PPT
Federal Register Vol. 74, No. 218, “Proposed Policy Statement on the Eligibility of Pedestrian and Bicycle Improvements Under Federal Transit Law.”

## Slide 13: Street Networks and Access
Most transit passengers access their stop by walking ¼ mile or less
However, the network structure will make this walk less direct
Network Structure | Percent of ¼ Mile Area Accessible in Walking Distance
Grid | 64%
Hybrid | 54%
Cul-de-sac | 28%
Notes: Walking is the most common mode used to reach transit, so ideally the street network should facilitate easy pedestrian access. In reality, though, there is a large discrepancy in how effective the different types of street networks work. Walking trips – and trips in mixed-traffic transit as well – can be more direct in a grid system than in a curvilinear cul-de-sac layout. As a result, it is much more difficult to run transit successfully in suburban areas with cul-de-sac street networks.
Source: Brail & Larrousse Bloustein Course

## Slide 14: Grid Network
Notes: Here is an example of the traditional grid street layout.
How easy would it be for a passenger to access transit in this area?
How easy would it be to provide transit service in this area?
Source: Brail & Larrousse Bloustein Course

## Slide 15: Hybrid Network
Notes: Here is an example of a hybrid between the cul-de-sac street network and a grid.
How easy would it be for a passenger to access transit in this area?
How easy would it be to provide transit service in this area?
Source: Brail & Larrousse Bloustein Course

## Slide 16: Cul-de-sac Network
Notes: Finally, here is an example of a curvilinear cul-de-sac street network. Note the street hierarchy, which often requires that you first travel to a major roadway before you can turn off to reach a local destination.
How easy would it be for a passenger to access transit in this area?
How easy would it be to provide transit service in this area?
Source: Brail & Larrousse Bloustein Course

## Slide 17: Selecting Roadways for Bus
Minimum lane width 11 ft
Minimum turning radius at intersections
Collector streets should be avoided
University Place, WA
Notes: Discuss the considerations in selecting roadways appropriate for a bus route.
Residents may be unhappy if a bus is routed down a quiet local road. Bus drivers are also an important constituency to consult when selecting your service roadways, as they will have to execute your plan.
Image:
http://www.flickr.com/photos/completestreets/3772442248/

## Slide 18: Transit Network Concepts
Radial – Focused on the downtown
Grid – Straight parallel routes spaced at regular intervals crossed by another set of routes (may require transfers)
Trunk lines with feeders – Arterial main line with separate branch lines
Through routing – All buses downtown which are then looped and sent back out
Transit centers – Lines converging at transit centers to facilitate transfers
Notes: Now we shift to the transit route network. There are a variety of network design concepts to consider – most common are the radial design and the grid design.
Other principles worth noting are the usage of trunk and feeder routes, the idea of linking two different routes through a downtown, and the use of transit centers to facilitate transfers.
Source: Brail & Larrousse Bloustein Course

## Slide 19: Radial Network
Notes: The main feature of a radial network is that all of the routes converge in the downtown, and then spread out to serve outlying parts of the city.
Source: Brail & Larrousse Bloustein Course

## Slide 20: Radial Network
Pros:
  Serves the central area very well
  Ideal for cities with a very dominant downtown
Cons:
  Service may be very indirect for outlying areas
Variations: Cities with multiple activity centers may use more of a “web” or “hub and spoke”
Notes: A radial design makes the most sense when a central area really does have the demand for a higher level of service compared with the rest of the city.
The main drawback to a radial system design is that travel between outlying areas will require travelers to go downtown and catch a transfer. In some cases this may be addressed with “beltway” or cross-suburban connectors.
The radial approach also becomes more complicated when you have a polycentric city with multiple areas that could be considered as downtown. Each of these can become the center of its own radial system, and the various lines can connect into a sort of spiderweb structure.

## Slide 21: Grid Network
Notes: The grid structure is easy to understand and predictable for travelers: one set of routes run north-south, another set runs east-west. It gives consistent coverage over a broad area, and it allows a traveler to go between any two points using a single transfer.
Source: Brail & Larrousse Bloustein Course

## Slide 22: Grid Network
Pros:
  Provides broad service coverage and access
  Ideal for cities with evenly distributed travel demand
Cons:
  Transfers will be quite common
Notes: This system makes the most sense in an area where demand is evenly distributed rather than concentrated in one place. It gives every part of the service area a fairly even level of service coverage.
A grid network relies on high-frequency service to facilitate easy transfers – if the transfers are not convenient a grid system will have trouble. This requirement also means a grid will only be feasible in relatively high-demand areas.

## Slide 23: Trunk and Feeder Network
Notes: Trunk and feeder systems often are found along major corridors. For example, the trunk line might be a commuter rail line or a BRT line, and the feeder service might consist of neighborhood shuttles or employer shuttles. The trunk service must be attractive enough to justify spending time on the feeder service rather than going directly to your destination.
Source: Brail & Larrousse Bloustein Course

## Slide 24: Through Routing
Notes: In a radial system, the routes branch outwards from the CBD – but it is preferable not to have them end there. Instead, you can link the downtown termini of two different routes to create one longer one. This is more efficient from a service perspective, and it can eliminate a transfer for those travelers who are headed to the suburbs.
Source:
TriMet

## Slide 25: Transit Center Approach
Without Transit Center
CBD
Route A
Route B
Route C
With Transit Center
Transit Center
CBD
Route A
Route B
Route C
Notes: Transit centers facilitate transfers between routes without having to go to the CBD. Where there is significant travel between outlying areas, creating this secondary node can make suburb-to-suburb travel easier.
Timed Transfers = Routes are designed to stop at the same location at the same time, wait for several minutes to allow for transfers, and then continue. This can dramatically reduce wait time for travelers making transfers.
Source:
TriMet

## Slide 26: Using “Pulse” Timed Transfers
Passengers hate waiting for a transfer – they perceive it as twice as stressful as time on-board a vehicle
Making transfers convenient can extend the reach of a network
Timed transfer example:
8:25 Buses A and B arrive
Passengers make an easy transfer…
8:30 Buses A and B depart
Notes: Even if your system can’t afford to provide very frequent service, you can still extend the reach of your network by coordinating the different routes with timed transfers. This is especially useful in a grid network where there will be many transfer opportunities.
But it is well established that passengers find transfers very stressful – twice as stressful as spending time on-board the vehicle. So to make a successful transfer-based system, it is crucial to make the transfers as easy as possible:
  Timed transfers can be used, in which different routes arrive at a point at the same time, wait a short time to give passengers the opportunity to transfer, and then depart again.
  Transfers can be provided to passengers for free, and this can be facilitated using transfer facility – where passengers already inside the facility don’t need to pay another fare to board another service (commonly used in subways.)
Sources:
Mees, Paul. “Transport for Suburbia.” 2009.
Horowitz, Alan J. "Subjective Value of Time in Bus Transit Travel." Transportation 10.2 (1981): 149-64.
Image:
http://ralphpugay.com/paintings/bus_transfer.jpg

## Slide 27: Intermodal Coordination
Notes: It’s important to recognize that public transit is just one piece of a broader network that includes many modes. Coordinating the connections between these modes is an important consideration for service planners.
We will briefly touch on the most common intermodal connections.

## Slide 28: Transit and Transit
San Diego, CA
Notes: Connections between different types of transit service are also important to consider. Bus stops at rail stations are often used; the bus route acts as a feeder to the rail service.
It is true that having to make a transfer can discourage people from riding transit, so when a transfer is necessary service planners should make it as simple and painless as possible. For example, coordinating timetables between the connecting services can save some passenger travel time.
Image:
http://www.flickr.com/photos/hercwad/3112256721/

## Slide 29: Transit and Autos
Harpers Ferry, WV
Notes: Park and rides allow travelers to drive part of their journey, then park their car and take transit the rest of the way. It is a common approach on the suburban outskirts of a transit network, where transit ridership can be closely tied to the parking availability.
The auto-transit connection can also be facilitated with “kiss and rides,” or designated curbside spaces for a traveler to get dropped off or picked up at a station.
Image:
http://www.flickr.com/photos/afagen/5214865055/

## Slide 30: Transit and Bicycles
Notes: Bicycle usage is slowly growing in the United States, and transit agencies should support this. Providing bike parking at stations and using vehicles that can hold bikes are two ways to make transit more convenient for bicyclists. Agencies can also assess the bicycle-friendliness of station areas using a bicycling LOS – a couple methods of measuring this have been published.
Some transit agencies also allow bicycles on-board rail vehicles to support intermodal travel. There are also agencies that have decided not to allow this, or to only allow it during off-peak times, based on the space that bicycles take up in the train. This is an issue that each agency should evaluate based on their particular context.
Images:
http://www.flickr.com/photos/anabananasplit/4879744408/
http://www.flickr.com/photos/cbnsp/4495126815/

## Slide 31: Transit and Pedestrians
Notes: And most crucially, transit stations and stops must provide good pedestrian access. This means a continuous sidewalk connection and a safe, well-lit place to wait at a bus stop. If the stop or station is at a busy roadway, there should be a safe crossing provided nearby for pedestrians. One way to measure pedestrian accessibility is using a “walkability” index or LOS – a couple methods of measuring this have been published.
ADA accessibility is an important consideration as well, particularly in selecting transit vehicles.
Images:
http://www.flickr.com/photos/komunews/4952326992/
http://www.flickr.com/photos/ewheeling/216301458/